## Slide 1: Computer Architecture Guidance
Keio University
AMANO, Hideharu
hunga@am．ics．keio．ac．jp

## Slide 2: Contents
Techniques on Parallel Processing
  Parallel Architectures
  Parallel Programming → On real machines
Advanced uni-processor architecture
  → Special Course of Microprocessors
  (by Prof. Yamasaki, Fall term)

## Slide 3: Class
Lecture using Powerpoint
  The ppt file is uploaded on the web site http://www.am.ics.keio.ac.jp, and you can down load/print before the lecture.
  Please check it on every Friday morning.
Homework: mail to: hunga@am.ics.keio.ac.jp

## Slide 4: Evaluation
Exercise on Parallel Programming using GPU (50%)
  Caution! If the program does not run, the unit cannot be given even if you finish all other exercises.
  This year a new GPU P100 is now under preparation.
Homework: after every lecture (50%)

## Slide 5: glossary 1
英語の単語がさっぱりわからんとのことなので用語集を付けることにする。
このglossaryは、コンピュータ分野に限り有効である。英語一般の使い方とかなり異なる場合がある。
Parallel: 並列の 本当に同時に動かすことを意味する。並列に動いているように見えることを含める場合をconcurrent(並行）と呼び区別する。概念的にはconcurrent > parallelである。
Exercise: ここでは授業の最後にやる簡単な演習を指す
GPU: Graphic ProcessingUnit Cell Broadband Engineを使って来たが、2012年からGPUを導入した。今年は新型でより高速のを使う予定

## Slide 6: Computer Architecture 1 Introduction to Parallel Architectures
Keio University
AMANO, Hideharu
hunga@am．ics．keio．ac．jp

## Slide 7: Parallel Architecture
Purposes
Classifications
Terms
Trends
A parallel architecture consists of multiple processing units
which work simultaneously.
→ Thread level parallelism

## Slide 8: Boundary between Parallel machines and Uniprocessors
ILP(Instruction Level Parallelism)
  A single Program Counter
  Parallelism Inside/Between instructions
TLP(Thread Level Parallelism)
  Multiple Program Counters
  Parallelism between processes and jobs
Uniprocessors
Parallel Machines
Definition
Hennessy & Petterson’s
Computer Architecture: A quantitative approach

## Slide 9: Multicore Revolution
Niagara 2
The end of increasing clock frequency
  Consuming power becomes too much.
  A large wiring delay in recent processes.
  The gap between CPU performance and memory latency
The limitation of ILP
Since 2003, almost every computer
became multi-core.
Even smartphones use 2-core/4-core
CPU.

## Slide 10: End of Moore’s Law in computer performance
1.25/year
1.5/year=Moore’s Law
1.2/year
No way to increase performance other than
Increasing the number of cores

## Slide 11: Purposes of providing multiple processors
Performance
  A job can be executed quickly with multiple processors
Dependability
  If a processing unit is damaged, total system can be available： Redundant systems
Resource sharing
  Multiple jobs share memory and/or I/O modules for cost effective processing：Distributed systems
Low energy
  High performance even with low frequency operation
Parallel Architecture: Performance Centric!

## Slide 12: Low Power by using multiple processors
n X performance with n processors,
  but the power consumption is also n times.
  If so, multiple processors does not contribute at all.
Pdynamic ∝ Vdd2 × f
fmax ∝ Vdd
If n processor achieves n times performance, fmax can be 1/n. → Vdd can be lowered. → Pdynamic can be lowered.

## Slide 13: Quiz
Assume a processor which consumes 10W with 1.8V Vdd and 3GHz clock.
You can improve performance by 10x with 10 processors, it means that the same performance can be achieved with 300MHz clock.
In this case, Vdd can be 1.0V.
How much power does the machine with 10 processors consume?

## Slide 14: glossary 2
Simultaneously: 同時に、という意味でin parallelとほとんど同じだが、ちょっとニュアンスが違う。in parallelだと同じようなことを同時にやる感じがするが、simultaneouslyだととにかく同時にやればよい感じがする。
Thread: プログラムの一連の流れのこと。Thread level parallelism（TLP)は、Thread間の並列性のことで、ここではHennessy and Pattersonのテキストに従ってPCが独立している場合に使うが違った意味に使う人も居る。これに対してPCが単一で命令間にある並列性をILPと呼ぶ
Dependability: 耐故障性、Reliability(信頼性）, Availability(可用性）双方を含み、要するに故障に強いこと。Redundant systemは冗長システムのことで、多めに資源を持つことで耐故障性を上げることができる。
Distributed system:分散システム、分散して処理することにより効率的に処理をしたり耐故障性を上げたりする

## Slide 15: Flynn’s Classification
The number of Instruction Stream： M(Multiple)/S(Single)
The number of Data Stream：M/S
  SISD
    Uniprocessors（including Super scalar、VLIW）
  MISD： Not existing（Analog Computer）
  SIMD
  MIMD
He gave a lecture at Keio
in the last year

## Slide 16: SIMD (Single Instruction Stream Multiple Data Streams
Instruction
Instruction
Memory
Processing Unit
Data memory
All Processing Units executes the same instruction
Low degree of flexibility
Illiac-IV/MMX instructions/ClearSpeed/IMAP/GP-GPU（coarse grain）
CM-2,（fine grain）

## Slide 17: Two types of ＳＩＭＤ
Coarse grain：Each node performs floating point numerical operations
  Old SuperComputers: ILLIAC-IV，BSP,GF-11
  Multimedia instructions in recent high-end CPUs
  Accelerator: GPU, ClearSpeed
  Dedicated on-chip approach: NEC’s IMAP
Fine grain：Each node only performs a few bits
operations
  ICL DAP, CM-2，MP-2
  Image/Signal Processing
  Connection Machines （CM-2) extends the application to Artificial Intelligence (CmLisp)

## Slide 18: GPGPU(General-Purpose computing on Graphic ProcessingUnit)
  Titan (NVIDIA K20X, 3rd place of Top500)
  TSUBAME2.5(NVIDIA K20X )
  A lot of supercomputers in Top500 use GPU.
※()内は開発環境
Notes: 18
近年、CPUとGPUやCELLといったマルチコアアクセラレータを組み合わせて使うハイブリッドの計算環境が普及しています。
例えばTOP500を見ると、TSUBAMEのNVIDIA GPUはもちろんですが、↑こういったATIのGPUを使ったスパコンも存在します。
またCell B.E.を搭載したアクセラレータもあります。
これらのアクセラレータを使って高い性能が得られるのですが、アクセラレータごとに異なる環境を用いなければなりませんでした。
そこで、Open CLという開発環境が登場しました。
OpenCLは、マルチコアプロセッサ向けの共通プログラミング環境で、Open CLにより、
異なるアーキテクチャでもCライクの同一ソースコードで開発が可能になりました。

## Slide 19
PBSM
PBSM
Thread Processors
PBSM
PBSM
Thread Processors
PBSM
PBSM
Thread Processors
PBSM
PBSM
Thread Processors
PBSM
PBSM
Thread Processors
…
Thread Execution Manager
Input Assembler
Host
Load/Store
Global Memory
GeForce
GTX280
240 cores
GPU is not just a simple SIMD.
A mixture of SIMD/MIMD/Multithread

## Slide 20: GPU(NVIDIA’s GTX580)
512 GPU cores ( 128 X 4 )
768 KB L2 cache
40nm CMOS 550 mm^2
128 Cores
128 Cores
128 Cores
128 Cores
L2 Cache

## Slide 21: The future of SIMD
Coarse grain SIMD
  GPGPU became a main stream of accelerators.
  Other SIMD accelerators are hard to be survive.
  Multi-media instructions will have been used in the future.
Fine grain SIMD
  Advantageous to specific applications like image processing
  On-chip accelerator

## Slide 22: MIMD
Processors
Memory modules (Instructions・Data）
Each processor executes individual instructions
Synchronization is required
High degree of flexibility
Various structures are possible
Interconnection
networks

## Slide 23: Classification of MIMD machines Structure of shared memory
UMA(Uniform Memory Access Model）
  provides shared memory which can be accessed from all processors with the same manner.
NUMA(Non-Uniform Memory Access Model）
  provides shared memory but not uniformly accessed.
NORA/NORMA（No Remote Memory Access Model）
  provides no shared memory. Communication is done with message passing.

## Slide 24: UMA
The simplest structure of shared memory machine
The extension of uniprocessors
OS which is an extension for single processor can be used.
Programming is easy.
System size is limited.
  Bus connected
  Switch connected
A total system can be implemented on a single chip
On-chip multiprocessor
Chip multiprocessor
Single chip multiprocessor→ Multicore
IBM Power series
NEC/ARM chip multiprocessor for embedded systems

## Slide 25: An example of UMA：Bus connected
PU
PU
Snoop
Cache
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
shared bus
Snoop
Cache
SMP (Symmetric MultiProcessor),
On chip multiprocessor or multicore
Note that it is a logical image

## Slide 26: MPCore (ARM+NEC)
CPU
interface
Timer
Wdog
CPU
interface
Timer
Wdog
CPU
interface
Timer
Wdog
CPU
interface
Timer
Wdog
CPU/VFP
L1 Memory
CPU/VFP
L1 Memory
CPU/VFP
L1 Memory
CPU/VFP
L1 Memory
Interrupt Distributor
Snoop Control Unit (SCU)
Coherence
Control Bus
Duplicated
L1 Tag
…
IRQ
IRQ
IRQ
IRQ
Private
FIQ Lines
Private
Peripheral
Bus
L2 Cache
Private
AXI R/W
64bit Bus
SMP for Embedded
application
Notes: ４つのコアを搭載可能、共有データのキャッシングはスヌープで管理する

## Slide 27: SUN T1
Core
Core
Core
Core
Core
Core
Core
Core
Crossbar
Switch
FPU
L2
Cache
bank
Directory
L2
Cache
bank
Directory
L2
Cache
bank
Directory
L2
Cache
bank
Directory
Single issue six-stage pipeline
RISC with 16KB Instruction cache/
8KB Data cache for L1
Total 3MB, 64byte Interleaved
Memory

## Slide 28: Multi-Core (Intel’s Nehalem-EX)
8 CPU cores
24MB L3 cache
45nm CMOS 600 mm^2
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
L3 Cache
L3 Cache

## Slide 29: Heterogeneous vs. Homogeneous
Homogeneous: consisting of the same processing elements
  A single task can be easily executed in parallel.
  Unique programming environment
Heterogeneous: consisting of various types of processing elements
  Mainly for task-level parallel processing
  High performance per cost
  Most recent high-end processors for cellular phone use this structure
  However, programming is difficult.

## Slide 30: NEC MP211
ARM926
PE0
ARM926
PE1
ARM926
PE2
SPX-K602
DSP
DMAC
USB
OTG
3D
Acc.
Rot-
ater.
Image
Acc.
Cam
DTV
I/F.
LCD
I/F
Async
Bridge0
Async
Bridge1
APB
Bridge0
IIC
UART
TIM1
TIM2
TIM3
WDT
Mem. card
PCM
APB
Bridge1
Bus Interface
Scheduler
SDRAM
Controller
SRAM
Interface
On-chip
SRAM
(640KB)
PLL
OSC
Inst.
RAM
PMU
INTC
TIM0
GPIO
SIO
Sec.
Acc.
SMU
uWIRE
Camera
LCD
FLASH
DDR SDRAM
Ｍｕｌｔｉ－Ｌａｙｅｒ ＡＨＢ
Heterogeneous type UMA

## Slide 31: NUMA
Each processor provides a local memory, and accesses other processors’ memory through the network.
Address translation and cache control often make the hardware structure complicated.
Scalable：
  Programs for UMA can run without modification.
  The performance is improved as the system size.
Competitive to WS/PC clusters with Software DSM

## Slide 32: Typical structure of NUMA
Node １
Node 2
Node ３
Node ０
０
１
２
３
Ｉｎｔｅｒｃｏｎｎｅｃｔｏｎ
Ｎｅｔｗｏｒｋ
Logical address space

## Slide 33: Classification of NUMA
Simple NUMA：
  Remote memory is not cached.
  Simple structure but access cost of remote memory is large.
CC-NUMA：Cache Coherent
  Cache consistency is maintained with hardware.
  The structure tends to be complicated.
COMA:Cache Only Memory Architecture
  No home memory
  Complicated control mechanism

## Slide 34: Supercomputer 「K」
Core
Core
Core
Core
Core
Core
Core
Core
L2 C
Inter
Connect
Controller
Tofu Interconnect
6-D Torus/Mesh
SPARC64 VIIIfx Chip
4 nodes/board
24boards/Lack
96nodes/Lack
RDMA mechanism
NUMA or UMA+NORMA
Memory

## Slide 35
SACSIS2012 Invited speech

## Slide 36: Multicore Based systems
Copyright © 2012, Elsevier Inc. All rights reserved.
Implementing in shared L3 cache
  Keep bit vector of size = # cores for each block in L3
  Not scalable beyond shared L3
Distributed Shared Memory and Directory-Based Coherence
IBM Power 7
AMD Opteron 8430
Notes: The University of Adelaide, School of Computer Science
平成30年4月6日
Chapter 2 — Instructions: Language of the Computer
36

## Slide 37: Xeon Phi Microarchitecture
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
TD
TD
TD
TD
TD
TD
TD
TD
GDDR MC
GDDR MC
GDDR MC
GDDR MC
All cores are connected through the ring
interconnect.
All L2 caches are coherent with directory
based management.
So, Xeon Phi is classified into
CC (Cache Coherent) NUMA.
Of course, all cores are multithreaded, and provide 512 SIMD instructions.

## Slide 38: DDM(Data Diffusion Machine）
．．．
．．．
．．．
．．．
Ｄ

## Slide 39: NORA/NORMA
No shared memory
Communication is done with message passing
Simple structure but high peak performance
Cost effective solution.
Hard for programming
Inter-PU communications
Cluster computing
Tile Processors: On-chip NORMA for embedded applications

## Slide 40: Early Hypercube machine nCUBE2

## Slide 41: Fujitsu’s NORA AP1000(1990)
Mesh connection
SPARC

## Slide 42: Intel’s Paragon XP/S(1991)
Mesh connection
i860

## Slide 43: PC Cluster
Beowulf Cluster (NASA’s Beowulf Projects 1994, by Sterling)
  Commodity components
  TCP/IP
  Free software
Others
  Commodity components
  High performance networks like Myrinet / Infiniband
  Dedicated software

## Slide 44
RHiNET-2 cluster

## Slide 45
Tilera’s Tile64
Tile Pro, Tile Gx
Linux runs in
each core.

## Slide 46: All techniques are combined
Nodes with CPU (Multi-core) are connected with NORA/NORMA
  Clusters in data-centers.
Nodes with CPUs(Multi-core)+GPUs(SIMD/many-core) are connected with NORA/NORMA
  Tsubame (TIT) and other supercomputers
Nodes with Multi-core are connected with NUMA
  K-supercomputer

## Slide 47: Multi-core + Accelerator
Intel’s Sandy Bridge
AMD’s Fusion APU
I / O
System Agent
Core4
Core3
Core2
Core1
LLC
LLC
LLC
LLC
GPU
GPU 1
Video Decoder
Core 1
GPU 2
Core 2
memory
controller
Platform
Interface
Notes: 47

## Slide 48: glossary 3
Flynn’s Classification: Flynn(Stanford大の教授）が論文中に用いた分類、内容は本文を参照のこと
Coarse grain：粗粒度、この場合はプロセッシングエレメントが浮動小数演算が可能な程度大きいこと。反対がFine grain（細粒度）で、数ビットの演算しかできないもの
Illiac-IV, BSP, GF-11, Connection Machine CM-2，MP-2などはマシン名。SIMDの往年の名機
Synchronization:同期、Shared Memory:共有メモリ、この辺は後の授業で詳細を解説する
Message passing:メッセージ交換。共有メモリを使わずにデータを直接交換する方法
Embedded System:組み込みシステム
Homogeneous:等質な Heterogeneous：性質の異なったものから成る
Coherent Cache:内容の一貫性が保障されたキャッシュ、Cache Consistencyは内容の一貫性、これも後の授業で解説する
Commodity Component: 標準部品、価格が安く入手が容易
Power 5, Origin2000, Cray XD-1,AP1000,NCUBE などもマシン名。The earth simulatorは地球シミュレータ,IBM BlueGene/Lは現在のところ最速

## Slide 49: Terms(1)
Multiprocessors：
  MIMD machines with shared memory
  （Strict definition：ｂｙ Ｅｎｓｌｏｗ Ｊｒ．）
    Shared memory
    Shared I/O
    Distributed OS
    Homogeneous
  Extended definition: All parallel machines（Wrong usage）
Multicomputer
  ＭＩＭＤ machines without shared memory, that is ＮＯＲＡ／ＮＯＲＭＡ

## Slide 50: Term(2)
Multicore
  On-chip multiprocessor.
  Mostly UMA.
  Symmetric Multi-Processor SMP
    Historically, SMP is used for multi-chip multiprocessor
Manycore
  On-chip multiprocessor with a lot of cores
  GPUs are also referred as “Manycore”.

## Slide 51
Stored
programming
based
Others
ＳＩＭＤ
Ｆｉｎｅ ｇｒａｉｎ
Ｃｏａｒｓｅ ｇｒａｉｎ
ＭＩＭＤ
Bus connected UMA
Switch connected UMA
ＮＵＭＡ
Ｓｉｍｐｌｅ ＮＵＭＡ
ＣＣ－ＮＵＭＡ
ＣＯＭＡ
ＮＯＲＡ
Systolic architecture
Data flow architecture
Mixed control
Demand driven architecture
Multiprocessors
Multicomputers
Classification

## Slide 52: Exercise 1
Pezy’s supercomputer Gyoukou got the 4th place at TOP500 in 2017 November.
But, the president of Pezy was arrested for crime of fraud later.
It uses Pezy SC2 as an accelerator.
Which type is Pezy SC2 classified into ?
If you take this class, send the answer with your name and student number to hunga@am.ics.keio.ac.jp
You can use either Japanese or English.