## Slide 1: NUMA machines and directory cache mechanisms
AMANO,Hideharu
Textbook pp.７０～７９

## Slide 2: NUMA(Non-Uniform Memory Access model）
Providing shared memory whose access latency and bandwidth are different by the address.
Usually, its own memory module is easy to be accessed, but ones with other PUs are not.
All shared memory modules are mapped into a unique logical address space, thus the program for UMA machines works without modification.
Also called a machine with Distributed Shared Memory
⇔ A machine with Centralized Shared memory (UMA).
Notes: NUMA or non-uniform memory access model has shared memory but their access latency and bandwidth are different by the address. Usually, its own memory module is easy to be accessed but ones with others PUs are not. All shared memory modules are mapped into a unique logical address space, thus the program for UMA machines works without modification. They are called with distributed shared memory. It is an opposite concept of a machine with centralized shared memory or UMA.

## Slide 3: The model of NUMA
Node １
Node 2
Node ３
Node ０
０
１
２
３
Ｉｎｔｅｒｃｏｎｎｅｃｔiｏｎ
Ｎｅｔｗｏｒｋ
Unique address space
Notes: This diagram shows the model of NUMA. Each memory module is assigned into the unique address space. If the node 0 accesses the address area 0, it accesses its own memory module. But, if it wants to access the other address, the request must be transferred through the interconnection network. Thus, the latency is stretched, and the bandwidth is limited.

## Slide 4: NUMA with Multicore processors
Copyright © 2012, Elsevier Inc. All rights reserved.
Introduction
Notes: The University of Adelaide, School of Computer Science
令和2年5月10日
Chapter 2 — Instructions: Language of the Computer
4
In the recent servers, each node is a multicore, and its architecture is UMA which is introduced in the previous lesson.

## Slide 5: Variation of NUMA
Simple NUMA： cache coherence is not kept by the hardware（CM*,Cenju，T3D，RWC-1, Earth simulator）
CC (Cache Coherent)-NUMA： providing coherent cache.（DASH，Alewife, Origin, SynfinityNUMA, NUMA-Q, Recent servers）
COMA (Cache Only Memory Architecture) : No home memory（DDM,KSR-1)
Notes: NUMAs are classified into three categories. One is a simple NUMA. It can cache the memory attached to the other PUs, but the coherence is not kept. On the contrary, Cache Coherent NUMA provides the coherent cache. It must provide the hardware mechanism to keep the coherence, so it tends to be complicated. The last style is COMA. But the machines in this class is not used recently.

## Slide 6: Glossary 1
NUMA（Non-Uniform Memory Access model):
メモリへのアクセスが均一ではないモデル（アーキテクチャ）、今回のメインテーマで別名Distributed Shared Memory machine：分散共有メモリマシンとも呼ばれる。この言葉の逆の意味はCentralized Memory:集中共有メモリということになりUMAである
Cache-Coherent NUMA:キャッシュの一貫性がハードウェアで保証されているNUMA 後で説明するようにプロトコルが面倒
COMA(Cache Only Memory Architecture):キャッシュだけのメモリアーキテクチャという意味だがもちろんキャッシュだけで構成されているわけではなく、ホームメモリを決めないものをこのように呼ぶ

## Slide 7: Simple NUMA
A PU can access memory with other PUs/Clusters, but the cache coherence is not kept.
Simple hardware
Software cache support functions are sometimes provided.
Suitable for connecting a lot of PUs: Supercomputers : Cenju, T3D, Earth simulator, IBM BlueGene, Roadrunner, K, Fugaku
Why some supercomputers take the simple NUMA structure?
  Easy programming for wide variety of applications
  →Powerful interconnection network
Notes: First of all, the simple NUMA is introduced. Some supercomputers use this style. It has some benefits. I will introduce some of them.

## Slide 8: CM* （CMU：the late 1970’s） One of roots of multiprocessors
．．．
CM00
CM09
ｋｍａｐ
Slocal
Slocal is an address transform mechanism.
Kmap is a kind of switch.
PDP11 compatible
processors
Notes: CM*, developed by CMU in the late 1970’s, is a root of multiprocessors. They used PDP11 as a cluster, and provided an address transform mechanism called Slocal. The link from Slocal is connected with Kmap, a kind of switch. The memory in the other cluster can be accessed through the Kmap and Slocal.

## Slide 9: Cray’s T3D: A simple NUMA supercomputer (1993)
Using
Alpha 21064
Notes: Supercomputers have used this style. Cray’s Tera three D was a simple NUMA supercomputer.

## Slide 10: The Earth simulator (2002)
Notes: The Earth Simulator got the top 1 in the world 2002. A lot of cabinets are placed on the big building like a gym. The deep blue ones are for computational nodes and light blue ones are for interconnection networks.

## Slide 11: Earth Simulator (2002,NEC)
Vector Processor
Vector Processor
…
Vector Processor
0
1
7
Shared Memory
16GB
Vector Processor
Vector Processor
…
Vector Processor
0
1
7
Shared Memory
16GB
Vector Processor
Vector Processor
…
Vector Processor
0
1
7
Shared Memory
16GB
….
Interconnection Network (16GB/s x 2)
Node 0
Node 1
Node 639
Peak performance
40TFLOPS
Notes: It forms a node with 8 vector processors, and connects 639 nodes with a large crossbar switch. Since the performance of the interconnection network was huge, it achieved an efficient performance close to the peak performance.

## Slide 12
From IBM web site
IBM blue gene series
Also simple NUMA
Notes: IBM blue gene series BlueGene/L, P and Q also used simple NUMA structure. They are connected with 3-D torus network instead of the crossbar of the earth simulator.

## Slide 13: Supercompuer K
Core
Core
Core
Core
Core
Core
Core
Core
L2 C
Inter
Connect
Controller
Tofu Interconnect
6-D Torus/Mesh
SPARC64 VIIIfx Chip
4 nodes/board
24boards/Lack
96nodes/Lack
RDMA mechanism
NUMA or UMA+NORMA
Notes: Japanese super computer K uses a simple NUMA structure. It provides Remote DMA mechanism to send the data from other nodes.

## Slide 14: Cell（IBM/SONY/Toshiba）
SXU
LS
DMA
PXU
L1 C
L2 C
MIC
BIC
External
DRAM
Flex I/O
EIB: 2+2 Ring Bus
CPU Core IBM Power
2-way superscalar, 2-thread
SPE:
Synergistic Processing
Element
(SIMD core)
128bit(32bit X 4)
2 way superscalar
32KB+32KB
512KB
PPE
512KB Local Store
SXU
LS
DMA
SXU
LS
DMA
SXU
LS
DMA
SXU
LS
DMA
SXU
LS
DMA
SXU
LS
DMA
SXU
LS
DMA
The LS of SPEs
are mapped on
the same address
space of the PPE
Notes: The IBM/SONY/Toshiba developed cell broadband engine for their game machine play station 3. It was also used as several supercomputers. In this architecture, all local memory modules attached to eight SPEs are mapped into the same address space of the host processor address space.

## Slide 15: PEZY-SC –1/2 [Torii2015]
Host I/F &
Inter Processor I/F
ARM
x2
Prefecture
L3 cache 2MB
4x4 City
DDR4
DDR4
Prefecture
L3 cache 2MB
4x4 City
DDR4
DDR4
Prefecture
L3 cache 2MB
4x4 City
DDR4
DDR4
Prefecture
L3 cache 2MB
4x4 City
DDR4
DDR4
City
SFU
2x2 Village
L2 D cache 64KB
Village
PE
PE
L1 D cache
2KB
PE
PE
L1 D cache
2KB
3 hirarchical MIMD manycore:
4PE x 4(Village) x 16(City) x 4(Prefecture) = 1,024PE
Notes: Pezy SC 1 and 2 adopted a hierarchical structure. 4x4 cities which share the L3 cache form a prefecture. A city consists of 2x2 villages which share L2 cache, and a village is built by 4 PEs. 2PEs share the L1 cache. It can cache the main memory but coherence is only kept in each hierarchy. Although it has an interesting memory architecture, the company head was arrested for the illegal acquition of national research fund and the project was terminated.

## Slide 16: CC-NUMA
Directory management mechanism is required for coherent cache.
Early CC-NUMAs use hierarchical buses.
Complicated hardwired logic
  Stanford DASH、MIT Alewife、Origin、Sinfinity NUMA
Dedicated management processor
  Stanford FLASH（MAGIC)、NUMA-Q(SCLIC)、JUMP-1(MBP-light)
Notes: Unlike simple NUMAs, CC-NUMAs provide a directory management mechanism for keeping the coherent cache. Early CC-NUMAs were an extension of the snoop cache and had hierarchical buses. But, later it was replaced to the directory management system with a point-to-point network. Some used complicated hardware logic, others used dedicated management processors.

## Slide 17: Ultramax (Sequent Co.） An early CC-NUMA
．．．
．．．
Shared memory
Hierarchical bus
Cache
Hierarchical extension of bus connected multiprocessors
Hierarchical bus bottlenecks the system.
Notes: An early CC-NUMA used an extension of the snoop cache by introducing a hierarchical bus. Each cluster was a snoop cache connected multiprocessor, and the accesses for the other cluster uses hierarchical bus. With the similar protocol of the snoop cache also on the hierarchical bus, the cache coherence was kept. Apparently, this approach causes the traffic congestion of the hierarchical bus.

## Slide 18: Stanford DASH A root of recent CC-NUMAs
．．．
ＰＵ00
ＰＵ０３
Directory
Main Memory
Directory Coherent control、Point-to-Point connection
Release Consistency
SGI Power Challenge
router
2-D mesh with Caltech router
Notes: Stanford DASH introduced the directory coherent control mechanism, point-to-point interconnection and release consistency model which are used in the current servers. The cluster was SGI’s Power Challenge workstation and they attached the directory mechanism and the router. The router was developed in the Caltech university, and a simple 2-dimensional mesh network was used.

## Slide 19: SGI Origin
Hub Chip
Main Memory
Ｎｅｔｗｏｒｋ
Bristled Hypercube
Main Memory is connected with Hub Chip directly.
1 Cluster consists of 2 PEs.
Notes: SGI Origin is a commercial version of the DASH. The number of Processors in a cluster was reduced because of the rapid performance improvement of a processor. Hub chip which manages the directory were used, and they formed a bristled hypercube.

## Slide 20: SGI’s CC-NUMA Origin3000(2000)
Using R12000
Notes: This machine was working in the ITC of this campus. We developed parallel programs on this machine.

## Slide 21: Stanford FLASH
MAGIC
Main Memory
Ｎｅｔｗｏｒｋ
2D Mesh
R1000
MAGIC is a dedicated processor for protocol control.
2nd Level
Cache
Notes: Since the hardware which controls the coherence became so complicated, the Stanford university developed a dedicated chip which controls the cache coherence with its software.

## Slide 22: JUMP-1: massively parallel machine CC-NUMA
256 Clusters （16 in a real machine）
RDT Network
Cluster 0
Cluster 1
Cluster 2
Cluster 3
Cluster 255
FB0
FB1
FB2
HDTV
controller
Pixel Bus
CRT
I/O
Box 0
I/O
Box 1
I/O
Box 15
SCSI
SCSI
SCSI
LAN
I/O BOX:SPARCstation5
Notes: Jump-1, a CC-NUMA was developed by the Japanese national project by cooperation of seven Japanese Universities.

## Slide 23: A cluster of JUMP-1
RDT Network
RISC
Processor
L1 Cache
L2 Cache
RISC
Processor
L1 Cache
L2 Cache
RISC
Processor
L1 Cache
L2 Cache
RISC
Processor
L1 Cache
L2 Cache
Cluster Bus
MBP-light
Cluster
Memory
TAXI
I/O Network
STAFF-Link
RDT Router
Notes: Like a Stanford project, it sed a dedicated processor called MBP light for the cache coherent control. 4 SPARC processors are used to develop a cluster, and a special interconnection network called RDT or recursive diagonal torus was used as an interconnection network.

## Slide 24: JUMP-1 was developed with 7 universities
A system with 16 clusters
(Kyoto Univ.)
A system with 4 clusters
(Keio Univ.)
Notes: They are outlook of Jump-1. A first prototype with 4cluster and 16 processors were developed in Keio University. Later 16 clusters with 64 processors worked in Kyoto University.

## Slide 25: Xeon Phi Microarchitecture
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
Core
L2
Cache
TD
TD
TD
TD
TD
TD
TD
TD
GDDR MC
GDDR MC
GDDR MC
GDDR MC
All cores are connected through the ring
interconnect.
All L2 caches are coherent with directory
based management.
So, Xeon Phi is classified into
CC (Cache Coherent) NUMA.
Of course, all cores are multithreaded, and provide 512 SIMD instructions.
Chinese Supercomputer Tianhe-2 used it for its accelerator
but changed to domestic one later.
Notes: Xeon Phi microarchitecture is a CC-NUMA with directory control mechanism. It provides 8 cores each of which provide directory. L2 cache is kept coherent with this mechanism.

## Slide 26: Multicore Based systems
Copyright © 2012, Elsevier Inc. All rights reserved.
Implementing in shared L3 cache
  Keep bit vector of size = # cores for each block in L3
  Not scalable beyond shared L3
Distributed Shared Memory and Directory-Based Coherence
IBM Power 7
AMD Opteron 8430
Notes: The University of Adelaide, School of Computer Science
令和2年5月10日
Chapter 2 — Instructions: Language of the Computer
26
Some recent server used directory controlled CC-NUMA structure. Here directory is attached to each memory system.

## Slide 27: Distributed cache management of CC-NUMA
Cache directory is provided for the cache block of the home memory.
The cache coherence is kept by messages between nodes.
Invalidation type protocols are commonly used.
The protocol itself is similar to those used in snoop cache, but everything must be managed with message transfers.
Notes: The directly is provided for each cache block of the home memory, and the cache coherence is kept by messages between nodes.

## Slide 28: Cache coherent control（Node 3 reads）
Node １
Node 2
Node ３
Node ０
U
ｒｅｑ
Ｕ：Ｕｎｃａｃｈｅｄ
Ｓ：Ｓｈａｒｅｄ
Ｄ：Ｄｉｒｔｙ
Ｉ：Ｉｎｖａｌｉｄａｔｅｄ
Ｓ：Ｓｈａｒｅｄ
Ｄ：Ｄｉｒｔｙ
Notes: Let me explain the cache coherent control using the directory. Each directory entry for the home memory has the state of the block and the bit map which shows who has the copy of the block. There are three states: U, S and D. At first, the state is U. Each cache directory has also its state. We assume three states: I, S, and D.
Here, let’s assume Node 3 sends the request to the Node 0 home memory.

## Slide 29: Cache coherent control（Node 3 reads）
Node １
Node 2
Node ３
Node ０
Ｓ
１
Ｓ
Cache block
Notes: Node 0 replies it and sends the cache block to the requesting node 3. It also changes its state into S, and set 1 at the corresponding bit map. The state of the cache of the requesting node 3 turns its state into S.

## Slide 30: Cache coherent control（Node 1 reads）
Node １
Node 2
Node ３
Node ０
Ｓ
１
Ｓ
req
Cache block
１
Ｓ
Notes: The similar thing happens when node 1 issues the request. The cache block is sent back from the node 0, and the corresponding bit is set.

## Slide 31: Cache coherent control（Node 3 writes）
Node １
Node 2
Node ３
Node ０
Ｓ
Ｓ
Write request
Invalidation
Ａｃｋ
D
Ｓ
Ｗｒｉｔｅ
D
Ack
→ I
１
１
0
Notes: When node 3 wants to write the data into the cache block, it sends the write request message to the home node 0. It checks the directory and knows that node 1 has the same block. So, node 0 sends the invalidation message to node 1. Node 1 invalids its cache block and sends back the acknowledge signal to node 0. Node 0 changes home memory state to D, and reset the bit corresponding to node 1. Then it sends the acknowledge message to node 3. After receiving it, node 3 changes its cache state into D. After that node 3 can read and write the block without sending any messages.

## Slide 32: Cache coherent control （Node 2 reads）
Node １
Node 2
Node ３
Node ０
D
Ｄ
ｒｅｑ
Write Back Req
Cache block
Write Back
→ S
Reads
１
１
S
S
Notes: What happens when node 2 wants to the same memory address. It sends the home memory and the home node knows that it has been updated by the node 3 by checking the directory. So, node 0 sends the write back request message to node 3. Node 3 replies to send the updated cache block and changes its state to S. After writing back the data, node 0, the home node changes its sate into S and set the bit corresponding to Node 2. Then node 0 send the cache block to node 2. The cache state of node 2 becomes S.

## Slide 33: Cache coherent control （Node 2 writes）
Node １
Node 2
Node ３
Node ０
D
Ｄ
ｒｅｑ
Write Back Req
Cache block
Write Back
→ I
Writes
１
１
D
0
Notes: What happens node 2 sends the write request instead of the read request. Similar to the case of read request, node 3 writes back the cache block to the node 0 home memory. But the cache state becomes I. Node 0 changes its state into D and set the bit 2 instead of bit 3. After getting the cache block, node 2 changes its state into D.

## Slide 34: Quiz
Show the states of cache connected to each node and directory of home memory in CC-NUMA.
The node memory in node 0 is accessed:
  Node 1 reads
  Node 2 reads
  Node 1 writes
  Node 2 writes
Notes: Here is a quiz.

## Slide 35: Triangle data transfer
Node １
Node 2
Node ３
Node ０
D
Ｄ
ｒｅｑ
Write Back Req to
Node2
Write Back
→ I
Writes
１
１
D
MESI, MOSI like protocols can be implemented,
but the performance is not so improved.
0
Notes: In order to improve the performance, node 3 sends the cache block directly to the requesting node 2 instead of the home node 0. The node 2 writes the data directly and changes state into D. It is somehow similar to that of the ownership of the snoop protocol. Techniques proposed for the snoop cache can be used, but the performance improvement is not so large.

## Slide 36: Synchronization in CC-NUMA
Simple atomic operations (eg. Test&set) increase traffic too much.
Test and Test&set is effective, but not sufficient.
  After sending an invalidation message, traffic is concentrated around the host node.
Queue-based lock:
  linked list for lock is formed using directory for cache management.
  Only the node which can get a lock is informed.
Notes: Simple atomic operations increase traffic too much. Test and Test&Set is effective, but not enough. So, Queue-based lock is proposed.

## Slide 37: Traffic congestion caused by Test and Test&Set(x) (Node 3 executes the critical section)
Node １
Node 2
Node ３
Node ０
S
x=0→１:Ｓ
１
x=1:Ｓ
１
１
１
x=1:Ｓ
x=1:Ｓ
Critical section
Busy waiting
Busy waiting
Busy
waiting
Notes: Assume that node 3 executes the critical section, and other nodes are waiting for the releasing the synchronization variable x. Thanks to test and test&Set, each node executes busy waiting without sending messages.

## Slide 38: Traffic congestion caused by Test and Test&Set(x) (Node 3 finishes the critical section)
Node １
Node 2
Node ３
Node ０
S
x=0:D
１
x=1:Ｓ
１
１
１
x=1:Ｓ
x=1:Ｓ
release x
Write req
x=0→１:Ｓ
I
I
I
Invalidation
D
Notes: However, when the node 3 releases the critical section by writing x, it sends the write request to the home node. and the node 0 sends invalidation messages to all other nodes.

## Slide 39: Traffic congestion caused by Test and Test&Set(x) (Waiting nodes issue the request)
Node １
Node 2
Node ３
Node ０
D
x=0:D
１
x=1:Ｓ
x=1:Ｓ
x=1:Ｓ
Busy waiting
Busy waiting
Busy waiting
Reqests
Notes: After that, all nodes must reply the acknowledge messages, and requests again to get the synchronization variable x. All these operations require a lot of messages and causes the congestion around the home node.

## Slide 40: Queue-based lock : Requesting a lock
Directory
Lock pointer
node0
node1
node2
node3
req
req
lock
Notes: Queue-based lock provides the pointer to each node. When synchronization request is issued from node3, a link to get the lock is made, and the pointer is stored. When other nodes make a request, they are linked to the list in order.

## Slide 41: Queue-based lock: Releasing the lock
Directory
Lock pointer
node0
node1
node2
node3
release
lock
Notes: When node3 releases the synchronization variable, it changes the pointer so that it indicates the next node. So, lock, the right to access the critical section will move around the linked list.

## Slide 42: Directory structure
Directory Methods
  Full Map directory
  Limited Pointer
  Chained Directory
  Hierarchical bit-map
Recent CC-NUMAs with multicore nodes is small scale, and the simple full map directory is preferred.
  The number of cores in a node is increasing rather than the number of nodes.
Notes: Directory at the home memory tends become large, because the total size of the memory is much larger than cache.
In order to reduce the memory requirement, various methods have been proposed.

## Slide 43: Full map directory
Node １
Node 2
Node ３
Node ０
S
１
１
Bit = Nodes
If the size is large, a large memory is required.
Used in Stanford DASH
Notes: The basic method which I introduced is called the full map directly. In this method, the number of bits are the same ss the number of nodes.

## Slide 44: Limited Pointer
Node １
Node 2
Node ３
Node ０
S
Using pointers
Notes: Instead of the bit-map, how about providing pointers. In this example, two pointers to provide to store the node number.

## Slide 45: Limited Pointer
Limited number of pointers are used.
  A number of nodes which share the data is not so large (From profiling of parallel programs)
If the number of nodes exceeds the pointers,
  Invalidate （eviction）
  Broadcast messages
  Call the management software (LimitLess)
    Used in MIT Alewife
Notes: The apparent problem is that the number of nodes which share the data is limited. But how can we do when the number of nodes exceeds the pointers. Some methods have been proposed. One is called eviction. It invalidates one of pointer. But it of course may cause the performance degradation when the evicted node sends the request again. Another method is to give up keeping the shared nodes. That is, invalidation messages are broadcasted to all nodes. This invalidation messages are just discarded if the node is not related, but it may cause the traffic congestion. The third method is to invoke the management software. It was used in MIT Alewife.

## Slide 46: Linked List
Node １
Node 2
Node ３
Node ０
S
Note that the pointer is provided in cache
Notes: An alternative method is to make a linked list between nodes who want to share the block like the queue based lock.

## Slide 47: Linked List
Pointers are provided in each cache.
Small memory requirement
The latency for pointer chain often becomes large.
Improved method: tree structure
SCI(Scalable Coherent Interface)
Notes: It requires relatively long time to manage and to trace the pointer chain. The improvement method to make the tree link structure was proposed. However, the benefit of method is small resource requirement. So, it is adopted in the standard protocol called SCI.

## Slide 48: Hierarchical bitmap
１０１
０００
００１
００１
０００
０００
１１
１０１
１００
S
S
S
S
Notes: If the network has hierarchical structure, the directory can be held at the branch of the hierarchy. It was adopted in COMA machine explained later. The problem is that it requires more amount of memory than the simple bit-map method.

## Slide 49: RHBD(Reduced Hierarchical Bitmap Directory) → A Course grain method
X
１０１
１０１
１０１
１０１
１０１
１０１
１１
１０１
１０１
S
S
S
S
X
X
X
Notes: In order to reduce the required amount, a course grain method can be used. For example, we can use the same bitmap at the all branch of the same hierarchy.

## Slide 50: Pruning Cache
X
X
１０１
１０１
１０１
101
１０１
101
１１
１０１
S
S
S
S
X
X
101
→100
→000
→001
→ 001
Notes: The problem is the method is increasing unnecessary invalidation message, to cope with the problem, we can introduce a kind of cache mechanism to the directory itself. This idea to introduce the cache can be used for the basic bit-map.

## Slide 51: COMA(Cache Only Memory Machine)
No home memory and every memory behaves like cache (Not actual cache)
Cache block gathers to required clusters. Optimal data allocation can be done dynamically without special care.
When miss-hit, the target block must be searched.
DDM、KSR-1
Notes: OK. The last type of the NUMA is COMA. Of course it takes a large cost if there is only cache memory. It means that there is no home memory and every memory behaves like cache. The cache block gathers to required clusters. That is an optimal data allocation can be done automatically. But, when miss-hit happens, the target block must be searched.

## Slide 52: DDM(Data Diffusion Machine）
．．．
．．．
．．．
．．．
Ｄ
First, check its own cluster
If not existing, go upward
×
Notes: The data diffusion machine uses hierarchical bitmap structure to manage the COMA system. If the block cannot be found to a hierarchy, the upper hierarchy is searched. It requires rather complicated handling if conflicts happen in the upper hierarchy.

## Slide 53: Glossary 2
Directly based cache protocol:ディレクトリを用いたキャッシュプロトコル、スヌープキャッシュではなく、ホームメモリ上のテーブル（ディレクトリ）を用いてキャッシュの一貫性を管理する方法
Full map directory:ディレクトリ管理法の一つ。PEに対応するビットマップをもつ
Limited Pointer:ディレクトリ管理法の一つ。限定された数のポインタを用いる。evictionは不足した場合、強制的に無効化する方法
Linked-list:リンクドリスト、ポインタの連鎖構造による管理法、SCI(Scalable Coherent Interface)はこれを用いたディレクトリ管理の標準規格
Queue-based lock:リンクドリストでロックの順番を管理する方法。NUMAの同期手法として一般的に用いられる。
Hierarchical:階層的、今回はバス構造、ディレクトリ構造のところで出てくる。

## Slide 54: Summary
Simple NUMA is used for large scale supercomputers
Recent servers use CC-NUMA structure in which each node is a multicore SMP.
  Directory based cache coherence protocols are used between L3 caches.
  This style has been a main stream of large scale servers.
Notes: Now, let’s make a summary of today’s lesson.

## Slide 55: Exercise
Show the states of cache connected to each node and directory of home memory in CC-NUMA.
The node memory in node 0 is accessed:
  Node 1 reads
  Node 3 reads
  Node 1 writes
  Node 2 writes
  Node 3 reads
  Node 3 writes
Notes: This is today’s exercise.