## Slide 1: Techniques for packet transfer in parallel machines
AMANO, Hideharu
Textbook pp.１６６－１８５
Notes: I have introduced direct and indirect networks. But, the techniques for packet transfer is more important for high speed data interchange.

## Slide 2: Packet transfer
Body
destination
length，source，etc．
Header
Flit
8bit~64bit
Packet switching
Circuit switching
Flit： Atomic unit for packet transfer
Flit width is not always link width.
Tailer: CRC etc.
Notes: The data transfer in parallel machines is classified into two methods: packet switching and circuit switching. The former method sends small data unit called a packet, while the latter method makes a circuit between a source node and destination node. Most machines use a packet switching because of its high efficiency. A unit data transferred in packet is called a flit. It is corresponding to word in a computer. A packet consists of header flits, body flits and tailor flits. Header carries information for the routing, for example, destination, length and source. The body carries data, and tailor includes error correcting code or information.

## Slide 3: Packet transfer method
Store and Forward
  Entire packet is stored in the buffer of each node
  TCP/IP protocol must use it
Wormhole routing
  Each flit can go forward as possible
  If the head is blocked, entire packet is stopped.
Virtual Cut Through
  If the head is blocked, the rest of packet is stored into the buffer in the node.
Notes: There are three methods. Store and forward, wormhole routing and virtual cut through.

## Slide 4: Store and Forward
All flits of packet are stored into the buffer in the node.
Large latency D(h+b)
Large requirement of buffer
Re-transmission of faulty packets can be done by the software
(TCP/IP uses this method)
Notes: In the store and forward routing, all flits of packet are stored into the buffer in every node. So, the latency becomes large. It becomes diameter by the total packet size, h for the header and b for the body. The buffer requirement is also large. However, node to node error check and re-transmission can be by software. That is, TCP/IP uses this method.

## Slide 5: Wormhole
The head of the packet can go as possible
Small latency hD+b
Small buffer requirement
Hardware router is required.
1
2
3
4
1
2
3
4
Notes: In the wormhole routing, the head of the packet can go as possible. The latency is small, it becomes h by D plus b. Since buffer only for the header is required, the total buffer requirement is small. It cannot be managed by software, that is, hardware router is required.

## Slide 6: Wormhole
The head of the packet can go as possible
Small latency hD+b
Small buffer requirement
Hardware router is required.
1
2
1
2
3
4
Notes: The header can go forward as possible.

## Slide 7: Wormhole
The head of the packet can go as possible
Small latency hD+b
Small buffer requirement
Hardware router is required.
1
2
3
4

## Slide 8: Wormhole
The head of the packet can go as possible
Small latency hD+b
Small buffer requirement
Hardware router is required.
1
2
3
4
Notes: In this method, once a packet is blocked it occupies buffers of a lot of nodes.

## Slide 9: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
1
2
3
4
1
2
3
4
Notes: In virtual cut through routing, all nodes have buffer for storing a packet as store-and-forward. But, the header can go forward as possible like wormhole routing. When the header is blocked, the rest of packet is stored in the buffer.

## Slide 10: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3

## Slide 11: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3

## Slide 12: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3

## Slide 13: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3

## Slide 14: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3

## Slide 15: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3

## Slide 16: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3

## Slide 17: Virtual Cut Through
If blocked, the rest of packet is stored in the buffer
The same latency as Wormhole
The same buffer requirement as Store and Forward
Hardware router is required.
2
4
1
3
Notes: Unlike the wormhole routing, buffer in the only one node is occupied when the packet is blocked.

## Slide 18: LAN,Component networks/SAN and Network on Chip
LAN(Local Area Network):
  Store and Forward
Component network/ SAN(System Area Network):
  The first generation NORA uses store and forward method.
  Recent Component networks/SANs:
    For large packets: Wormhole
    For multicast: Virtual Cut Through
  Infiniband
Network on Chip:
  Wormhole
Notes: Three packet forwarding methods are used for appropriate type of interconnection network. LAN or local memory network uses TCP/IP, that is store and forward. Component network and system area network used store and forward first, but wormhole or virtual cut through is used. For example, Infiniband uses the virtual cut through is used. For Network on chip, the wormhole routing is mainly used.

## Slide 19: Qiuz
A packet with 1 flit header and 15 flits body is transferred on a 4-ary 2-cube. Compute the largest number of clocks when it is sent with Store-and-Forward manner, and compared with the case when Wormhole method is used. Ignore the delay caused by congestion.
Notes: Here is a simple quiz.

## Slide 20: A problem of Wormhole
Notes: The problem of wormhole routing is that buffer in a lot of nodes are blocked by a packet. In this example, the destination buffer of the green packet is empty, but blocked because no buffer can be used in this node.

## Slide 21: Virtual Channel
By providing a bypass
buffer, channel is provided
virtually.
Notes: If there is reserved buffer for each direction, this green packet can go forward.

## Slide 22
It wants to turn right, but impossible
The lane for turning right
Wasted Bandwidth
Implementation of Virtual Channel
Notes: This idea is called the virtual channel. It is somehow like the dedicated lane for turning right. This car wants to turn right, and the target road is empty, but it is impossible to go.
If the lane for turning right is provided, the car can turn right.

## Slide 23: Implementation of Virtual Channel
VC → Providing another lane
  But the physical wires are not increased.
Wasted Bandwidth
[Dally,TPDS’92]
VC#0
Packet (a)
Packet (b)
VC#1
Notes: In order to do it, virtual channel provides independent channels. When this channel is blocked, another packet can go forward using the other channel. Note that the physical wires are not increased, but used in time multiplexing manner when not used by the blocking.

## Slide 24: Handshake of Virtual Channel
NODE
MUX
Ｂｕｆｆｅｒ
Ｂｕｆｆｅｒ
Handshake line
Handshake line
Link
Crossbar
Notes: In order to implement virtual channel, handshake mechanism is needed. That is, the information whether the buffer is empty or not must be transferred independently.

## Slide 25: An example of a modern router
WH router with two virtual channels
5x5 XBAR
ARBITER
FIFO
FIFO
FIFO
FIFO
FIFO
X+
X-
Y+
Y-
CORE
X+
X-
Y+
Y-
CORE
Notes: This shows an example of a modern router. There are two buffers for two virtual channels. Here, 5x5 router for two dimensional mesh is assumed. Core means the connected computing node. 5x5 crossbar and arbiter are provided.

## Slide 26: Pipelined operation
It takes three clocks to pass through the switch
  RC (Routing Computation)
  VSA (Virtual Channel / Switch Allocation)
  ST (Switch Traversal)
RC
VSA
ST
ST
ST
ST
RC
VSA
ST
ST
ST
ST
RC
VSA
ST
ST
ST
ST
ELAPSED TIME [CYCLE]
1
2
3
4
5
6
7
8
9
10
11
12
@ROUTER A
@ROUTER B
@ROUTER C
HEAD
DATA 1
DATA 2
DATA 3
Notes: The packet is transferred in the pipelined manner. This example uses three stages: routing computation, virtual channel and switch allocation stage, and switch traversal.

## Slide 27: Deadlock avoidance
Blocking destination buffer each other
To solve it
→ Eliminate cyclic dependency between buffers
Notes: Next, let me explain the problem of the deadlock. It is caused when each target buffer is blocked by each other. The red packet wants this buffer, the blue one wants this, but the green one wants this. So, they are mutually blocked. This happens when the dependency of buffer requirement forms a cycle. In order to solve it, we must eliminate cyclic dependency between buffers.

## Slide 28: Structured buffer pool
Packet is sent to Buf#＋１
No cyclic dependency between buffers
Structured channel for Wormhole
0
1
2
3
Notes: Structured buffer pool is a basic method to solve the deadlock. It provides a plenty of buffers, and the packet is sent to the buffer number+1. That is, this packet is transferred to buffer 1, then 2, and 3. Apparently no cyclic dependency between buffers is formed. However, it requires D+1 buffers where D is the diameter. The same concept can be used for the virtual channel. It is called a structured channel.

## Slide 29: Dimension order (e-cube) routing：DOR
Ｗ
Ｓ
Ｅ
Ｎ
The fixed order:
W→S→E→N
No cyclic dependency
Dedicated buffers
are provided for each
direction.
Notes: Dimension order routing or DOR fixes the order of dimension to be used. For example, first use x direction then use y direction. Of course, dedicated buffers are provided for each direction.

## Slide 30: Dimension order routing
Ｗ
Ｓ
Once the direction is changed,
it cannot be used again.
X
Notes: Dimension order routing does not allow to use the dimension again after using other dimension. That is, to use this dimension is forbidden.

## Slide 31: DOR for torus
Single direction packet transfer also makes a cyclic dependency
Packet A
Packet B
Notes: The DOR is guaranteed deadlock free in the mesh network. But, in the torus with wrap-around links, the cyclic dependency is formed even if the rule of kept.

## Slide 32: DOR for torus
1
０
Virtual channel number is changed when the round trip
link is used.
０
1
1
０
０
０
Notes: To solve it, virtual channel number is switched when the round trip link is used. With this simple rule, the DOR can be used. The DOR can be applied any structure of k-ary n-cube.

## Slide 33: Glossary 1
Flit:パケットの基本（最小）転送単位、必ずしもリンクのビット幅と等しい必要はないが、これ以上細かいデータ単位で転送を制御することはできないもの
Wormhole routing:いも虫が穴を開けながら進んで行く様子から出た単語。日本語でもこのまま読む。
Virtual Cut through:仮想的にパケットが突き抜けたように見えることから出た単語。日本語でもこのまま読む
Virtual Channel:仮想チャネル。バッファとハンドシェークラインを独立に用意することで、仮想的に複数の転送チャネルを実現する。リンクの利用率を上げ、デッドロックを防ぐ。
Deadlock:すくみ、デッドロック、パケットが用いるバッファがCyclic dependency（互いに循環的にバッファを要求すること）を生じることにより、先に進めなくなる現象
Structural buffer pool：構造化バッファ法、デッドロックを防ぐための古典的な手法
Notes: This is the glossary of the first segment.

## Slide 34: Adaptive routing
A fixed path is used, and not changed dynamically.
  Fixed/Deterministic routing
A path is dynamically changed in order to bypass the congested point (hot spot).
  Adaptive routing
  However, deadlock should be avoided.
Notes: When a fixed path between source and destination is always used, it is called a fixed or deterministic routing. On the contrary, a path is dynamically changed in the adaptive routing in order to bypass the congested point or hot spot. The challenge is to avoid to make a cyclic dependency selecting adaptive paths.

## Slide 35: Adaptive routing techniques
Using sub-networks
  double-Y routing
  Planner Adaptive routing
Using virtual channels
  Dimension reversal routing
  ＊channel (Duato’s Protocol)
Probability based methods
  Chaos routing
Restrict the direction of paths
  Turn model
Notes: For avoiding the deadlock, there are several methods, to use sub-networks or to use virtual channels. This chaos routing is interesting method to use the probability. The last one is by restricting the direction of paths.

## Slide 36: double Y routing
+X subnet
-X subnet
Using virtual channels, a network is
divided into two sub-networks.
Cyclic redundancy can be eliminated
if a packet uses only a sub-network.
Notes: In this double Y routing by using virtual channels, a network is divided into two sub-networks. +X subnet and –X subnet. If a packet uses only a sub-network in a direction, the deadlock never happens.

## Slide 37: Dimension reversal routing
Providing N virtual channels, and start from channel N.
DOR-cube routing is basically used.
When the packet is routed to the direction which is forbidden in the DOR routing, then decrement the virtual channel number.
On channel 0, DOR is strictly used.
Notes: Dimension reversal routing uses N virtual channels, and starts from channel N. DOR routing is basically used, and when the packet is routed to the direction which is forbidden in the DOR routing, then decrement the virtual channel number. On the channel 0, DOR must be used, that is it is not an adaptive routing anymore.

## Slide 38: Dimension reversal routing
Ch.2
Ch.2
Ch.1
Ch.1
When a packet goes
to irregular direction,
the virtual channel
number is decremented.
Ch.1
Ch.0
Ch．0 must use DOR
routing
Notes: This is an example of dimension reversal routing. When a packet goes to irregular direction, the virtual channel number is decremented.

## Slide 39: Ｔｕｒｎ ｍｏｄｅｌ: Motivation
Ｘ
DOR routing forbids too many turns.
Cycles can be broken with less forbidden turns.
Ｘ
Ｘ
DOR routing which allows only W→S→E→N
W
W
Ｘ
S
S
E
E
N
N
Notes: The DOR routing decides the order of turn strictly. That is, it forbids too many turns. In order to break the cycle, less forbidden turns are enough. Turn model tries to find the minimum set of the forbidden turns.

## Slide 40: Forbidden turns must be set considering complex combinations
Ｘ
Ｘ
Ｘ
Ｘ
A Cycle is formed
with a combination.
Notes: We must take care of complex combinations of multiple cycles. For example, the combination of these forbidden turns still forms this cycle.

## Slide 41: Deadlock free set of forbidden turns
Ｘ
Ｗｅｓｔ Ｆｉｒｓｔ
Ｎｏｒｔｈ Ｌａｓｔ
Ｘ
Ｘ
Ｘ
Notes: West first routing forbids these two turns. That is, west direction cannot go after turning. It means the west must be selected first. In north last routing, once the north direction is selected, it cannot turn any direction. That is the north must be selected last. However, they still have room of changing direction unlike the DOR.

## Slide 42: Congestion avoidance with Ｗｅｓｔ Ｆｉｒｓｔ
Ｘ
Once a packet goes to West and turns, it cannot go again.
Ｎ
Ｗ
Ｅ
Ｓ
Notes: Assume that this link is faulty or congested. We must bypass the node by using the west first method. Note that the turn model is non-minimal routing which can select non-minimal paths.

## Slide 43: Ｄｕａｔｏ’ｓ Ｐｒｏｔｏｃｏｌ （*-channel）
ＣＡ２
ＣＡ１
ＣＡ０
ＣＡ３
Ｅｓｃａｐｅ Ｐａｔｈ
Notes: Duato’s protocol or *-channel makes the best use of virtual channels. By using the VC, two paths are provided. The adaptive path and the escape path. The adaptive path can have a cyclic path but the escape path must include the all nodes but be deadlock free. The move from adaptive path to escape path is free. If adaptive path causes the deadlock, it moves the escape path. Since escape path is deadlock free, the deadlock on the adaptive path will be solved anyway.

## Slide 44: Minimal routing [F.Silla,1997]
Overall the network, a path without cycle is provided. (Escape path)
A packet can be moved from Adaptive path to Escape path at any node.
Once a packet uses Escape path, it cannot go back to Adaptive path
Src
Escape Paths
Adaptive Paths
Dst
Notes: The condition is as follows. Escape path must be overall the network and without cycle. Also, a packet can be moved from adaptive path to escape path at any node. Once a packet uses Escape path, it cannot go back to the adaptive path.

## Slide 45: Adaptive routing for Irregular networks: Up*/Down* routing
Typical partially adaptive routing
Eliminates a channel cyclic-dependency in order to avoid deadlock.
Algorithm:
  Build a spanning-tree.
    BFS(Breadth First Search)
    DFS(Depth First Search)
  Build an up/down directed-graph.
  Set a restriction to avoid the deadlock.
Notes: Irregular networks have no regular to build the topology. The up*/down* routing is a famous adaptive routing used in any network. First, a spanning tree is built. Both breadth first search and depth first search can be used. Then an up/down direction is attached. By restricting the turn from down to up direction, the deadlock is avoided.

## Slide 46: Building an up*/down* directed graph
7
1
2
4
0
8
5
6
3
2. Add the rest nodes to the tree.
2
1
1
2
5
4
6
3
3
4
5
6
8
7
7
8
1. Select a root node.
Root
0
0
Spanning tree
3. Allocate the direction (up or down) for each channel.
a. Up direction
destination node is closer to the root node.
b. Down direction
depth 0
depth 1
depth 2
depth 3
Bi-directional channel
Notes: Spanning tree can be built as follows. First, select a root node, and add other nodes to the shape of the tree. Then, the direction is attached to each link. Up direction is attached to the link when the destination node is closer to the root node. Down is attached to the opposite direction.

## Slide 47: Up*/Down* routing algorithm
Up
Down
After using up channel(if any),
use down channel(if any).
Non-minimal partially adaptive routing
1
0
2
3
4
5
7
6
8
down channel
up channel
A cyclic dependency between up and down channels is broken.
deadlock-free
Notes: The rule is simple. Aflter using up channel, use down channel. Assume that the source node is 3 and the destination node is 6. In this case, first, the packet must go to up direction and then go to down direction. The shorter, alternative route is not allowed to be used. Although a cyclic dependency is broken, it is non-minimal routing.

## Slide 48: Drawbacks of up*/down* routing
Many forbidden turns are concentrated on certain leaf nodes.
Congestion around root node.
Improvement proposals
  Using DFS tree
  Introducing another dimension
Notes: The up/down routing is general way, but there are following drawbacks. That is many forbidden turns are concentrated on certain leaf nodes. Congestion around the root node is another problem. Improvement methods have been investigated.

## Slide 49: Researches on adaptive routing for regular networks
Ｄｕａｔｏ’s Ｐｒｏｔｏｃｏｌ or Turn model is mostly used.
For irregular networks, up*/down* routing is also popular.
Deadlock detection and drop protocol vs. deadlock free routing.
Notes: Recently, Duato’s protocol or turn model is mostly used for regular networks. For irregular network, up/down routing is popularly used.

## Slide 50: Summary: adaptive routing
Drawbacks:
  FIFO assumption is not guaranteed.
  Difficult to debug, if trouble occurs.
However, the benefits will overcome the drawbacks.
Recent high performance networks use adaptive routing.
Notes: Let’s make a summary.

## Slide 51: Exercise
For an irregular network shown below:
  Pick up a node as a root node and draw a spanning tree.
  Add up/down direction to each link.
  Show the longest path between a source and destination node.
A
B
D
G
J
K
F
E
C
H
L
Notes: Today’s exercise is very simple.

## Slide 52: Glossary2
Adaptive routing:適応型ルーティング。ネットワークの混雑状況に応じて動的に経路を変えるルーティング。変えることができない方法をDeterministic routing（固定ルーティング）と呼ぶ。
  経路を勝手に変えるとデッドロックしてしまうので、様々な方法が提案されている。Double Y Routing、Dimension Reversal Routing,Turn model, Duato’s protocolは、全てこの方法の名前。
  Minimal routingつまり最短経路を必ず選ぶ方法と、non-minimal routing最短経路でなくても迂回可能な方法がある。
SAN(System Area Network): PCクラスタなどで用いられるネットワーク、代表選手はMyrinet、QsNet。ちなみにサーバー屋さんは、SANを（Storage Area Network)のことだと思っているので注意。
Irregular Network:不規則なネットワーク、多くのSANでは規則的ではなく、不規則なネットワークを許容する。これはPCクラスタなどでは、場合に応じて、ノードが欠けたりするため。