## Slide 1: Bus / Crossbar Switch
AMANO, Hideharu
hunga@am．ics．keio．ac．jp
Notes: Today, I am talking about the basic knowledge on buses and crossbar switches used in UMA or multi-core.

## Slide 2
CPU
L1 Cache
L2 Cache
L3 Cache
SRAM
Main memory
DRAM
～64KB 1-2clock
～256KB 3-10clock
2M～4MB 10-20clock
4～16GB 50-100clock
Memory Hierarchy
Locality is used.
Small high speed
Large low speed
Secondary Memory
μ-msec
TB
On-Chip cache
Transparent from Software
Managed by
Operating
System
Notes: First of all, let’s review on the memory hierarch. It makes the use of special and temporal locality of memory access. That is, a high speed but small memory is located near the CPU. L1 or level 1 cache is directly connected to the CPU, and L2 cache is located on the same chip. L3 cache is an on-board cache but recently it is also embedded in the same chip. These cache memory modules are all implemented with SRAM or static ram. The main memory is implemented with the dynamic RAM. From the main memory, all memory modules are transparent, that is, they have to be controlled by the hardware. The secondary memory is managed by the operating system. It has been built with magnetic disk, but recently, flush memory has taken place rapidly.

## Slide 3: Uni-processor structure
CPU
North
Bridge
South
Bridge
Graphics
DRAM
USB
Ether
Legacy I/O
PCI/PCIexpress
Memory Controller HUB
I/O Controller HUB
L1
L2
L3
Notes: The memory hierarchy is implemented with two types of bus or switch: North bridge and south bridge. They are Intel’s terminorogy. North bridge is a switch for high speed devices such as DRAMs and graphics processing unit. On the other hand south bridge is a bridge to I/O devices, USB, Ethernet and other legacy I/Os. PCIe bus is also connected.

## Slide 4: Sharing cache introduces congestion
PE
North
Bridge
South
Bridge
Graphics
DRAM
USB
Ether
Legacy I/O
PCI/PCIexpress
Memory Controller HUB
I/O Controller HUB
L1
L2
L3
PE
PE
PE
Notes: OK. What happens when a multicore is used instead of the uniprocessor? The simplest idea is to share the L1 cache. But, it is impossible because of the severe access contention at the L1 cache, since the L1 cache is very tightly connected to the processing element.

## Slide 5: The typical multicore structure
PE
North
Bridge
South
Bridge
Graphics
DRAM
USB
Ether
Legacy I/O
PCI/PCIexpress
Memory Controller HUB
I/O Controller HUB
L1
L3
PE
PE
PE
L1
L2
L1
L1
Snoop Cache
Bus
Crossbar
Notes: So, how about providing the private cache as the L1 cache and sharing the L2 cache. It is possible just if the cache coherence problem is solved. I will talk about this problem in the next lesson, and skip it today. Anyway, note that the bus is used to connect cores and the L2 cache. Of course, this bus is not a traditional passive bus.

## Slide 6: Implementation of buses
Multiplexer
Passive Bus：
Board level
implementation
Active Bus:
Chip level implementation
A single module sends data to all other modules
Notes: In old days, the bus is implemented with just wires pulled up registers for termination. This style of bus is still used for the back-plane bus of desktop computers. Various types of components can be connected but the operational speed tends to be slow.
Instead, buses in the chip is implemented with active gates. For example, a multiplexer is used in this case, it selects one of inputs data and distributes to all components. The definition of the bus is that anyone of the connected modules can send its data to all other members. This is sometimes called a multi-drop bus. In computers, only multi-drop buses are used.

## Slide 7: Requirements
High Performance
  Bandwidth（Throughput）
  Latency
Flexibility（Universality)
  The number of modules
  Clock frequency
  Electrical characteristics
Dedicated Bus
Standard Bus
Notes: There are inconsistent requirements to bus. First is high performance. The bandwidth or throughput indicates the total amount of data to be transferred in a cycle. The latency means the time from the sender starting data to the receiver receiving them. The high speed bus is needed to have a large bandwidth and short latency.
On the other hand, flexibility or universality is also required. That is, a bus is needed to connect a certain number of modules which use various clock frequency and electrical characteristics. Since it is difficult to satisfy both, we provide two types of buses: dedicated bus and standard bus in a system.

## Slide 8: System bus vs. I/O bus
System Bus
(Dedicated)
I/O Bus
(Standard)
Notes: Most of multicore system uses a dedicated system bus to connect cache system and high speed accelerators. Also it provides standard I/O bus through the bridge chip. North-and-South bridge structure which was introduced before is one of this example.

## Slide 9: Synchronous vs. Asynchronous
Synchronous bus
  Data is sent synchronized with a clock
    Easy to handshake, block (continuous) data transfer
    Module numbers/types are limited
  PCI、Mbus、PCIx、PCI express, On chip buses
  Performance centric
Asynchronous bus
  Data is sent without a system clock
    Variable modules can be connected
  VME、Futurebus+
Recently, asynchronous buses are not commonly used
Notes: Buses are sometimes classified into two categories: synchronous or asynchronous. In synchronous buses, data are sent synchronized with a clock. This bus can support a high speed block data transfer but modules numbers and/or types are limited. They must follow the fixed bus clock. On the contrary, in asynchronous buses, there is no system clock, and so every data transfer requires a handshake. However, this classification is rather old-fashioned. Recent buses are all synchronous bus, and asynchronous buses seem to be extencted.

## Slide 10: Terms around bus
Transaction: A continuous data transfer of address and data
Arbitration：An operation for taking a right to control the bus
Bus Master: a module which had a right of controlling the bus through the arbitration
Bus Slave：modules except the bus master
Notes: Now, let me explain some terms around bus.

## Slide 11: A sequence of data transfer with the bus
Get the mastership with the arbitration
Bus Transaction
  Address transfer
  Data transfer (repeated if necessary)
  End of transaction
Release the mastership
Arbiter hardware
Handshake
Notes: When you want to use a bus, first, you have to get the mastership with the arbitration. Then, you start the bus transaction. Usually, address and data are multiplexed, so first, address is transferred. At that time, handshake is needed between the master and slaves. Then, data transfer starts. Multiple data are often transferred iteratively synchronized with a clock in the synchronous bus. At the end of transaction, sometimes, data for error detecting or correction code are transferred. Then, the master releases the mastership, and the next transaction starts by another master.

## Slide 12: Arbiter
．．
Priority Encoder
Arbiter
Centralized
H
Distributed bus
Daisy Chain
Distributed
Centralized arbiter is used inside the chip
Notes: Arbiter is classified into centralized and distributed. The simplest centralized arbiter is a priority encoder. It selects a winner from multiple competitors. For multicores, since every module is embedded into a chip, the centralized arbiter is used.

## Slide 13
From
CMOS VLSI Design
by Weste and Harris
Centralized
Arbiter
=
Priority
Encoder
Tree
Notes: There are various types of priority encoders. They somehow, resemble to adders. The simplest one uses the ripple carry structure. Like the adder, it has the problem of long delay time. So, look ahead, incremented, and Skransky methods have been proposed to reduce the delay. Of course, they need extra hardware.

## Slide 14: Daisy Chain
If no request EI→EO
The request can be issued only if EI is H level
When the request is issued, EO becomes L level
EI
EO
EI
EO
EI
EO
EI
EO
EI
EO
H
H
H
H
H
Request
L
L
Request
X
Right side module has a low priority
Request
Left side module has a high priority
L
L
X
Notes: Daisy chain is the simplest arbiter. The modules are connected tandemly with the signals EI and EO. The rule is simple, if there is no requests, the module transfers the level of EI to EO. The request can be issued only if EI is High level, and negates EO. All the following modules’ EI turns Low, thus they cannot issue the request. Obviously, the leftmost module as the highest priority. Since this method is easy to implement, it is often used for an arbiter Direct Memory Access or DMA requests.

## Slide 15: Open Drain bus
‘H’
‘H’
OFF
OFF
OFF
OFF
If all inputs are ‘H’, the bus becomes ‘H’.
‘H’
‘H’
‘H’
‘H’
‘H’
OFF
OFF
OFF
OFF
If at least an input becomes ‘L’,
the bus becomes ‘L’ .
‘H’
‘H’
‘H’
ON
‘L’
‘L’
‘L’
ON
If multiple inputs become ‘L’
it still remains ‘L’,
Wired-OR(AND Tie)
Notes: The traditional backplane bus uses the open drain gate. In such a gate, the drain of output transistor is opened and connected together.
The high level is supplied through the termination resisters. In this case, if all transistors are off, the bus wire becomes high because it is pulled up by resisters.
If at least an input becomes low, the transistor turns on, and the level becomes low. The case of two or more transistors are ON, the same thing happens. Since at least an input becomes low, the wire is low. Thus, this mechanism is sometimes called Wired-OR. Some people call it AND Tie.

## Slide 16: Distributed bus arbiter
０ １ ２ ３ ４ ５ ６ ７
０
０
１
０
１
１
１
１
０
０ １ ２ ３ ４ ５ ６ ７
０
０
１
０
１
１
１
１
０
Check from the upper line.
If the value on the line is not equal to its output number, then stop the output.
Open Drain：
0 overtakes 1
Output its own number
Notes: By using open drain buses, a log2N distributed bus arbiter can be built. We need log2N buses for N modules. Here, there are 8 modules, so three wires are needed. Each module sends its own binary number to the bus. Here, assume that module 1, 3, and 6 issue the request.
Then, the bus is checked from the highest digit. If the level is not the same as its own level, it removes its request from all wires. In this case, the module six withdraws since it receives 0 instead of its issued 1. Then, the second wire is checked. This time 3 withdraws. Finally the module 1 wins.

## Slide 17: Modified method（Keio’s patent）
０ １ ２ ３ ４ ５ ６ ７
０
０
１
０
１
１
１
１
０
Output its own number
Ｘ
Ｘ
Ｘ
Ｘ
０ １ ２ ３ ４ ５ ６ ７
０
１
１
１
１
０
Parallel check is possible
Ｘ
Ｘ
Ｘ
Ｘ
０
０
１
Set cut-points on the bus
Notes: The problem of the distributed arbiter is it takes Log2N clocks to fix the result. Keio university invented the improved the method. The key of magic is to cut the wire and divides it into 4 segments and 2 segments like this.
Then the same algorithm is applied, but this time the winner can be selected just with a clock cycle, since 0 is not propagated beyond the cut. I think it is a good idea, and Keio University got a patent. Unfortunately, no one was interested in this idea and this patent was expired without getting any money.

## Slide 18: Starvation Problem
If the priority of the arbiter is fixed, a weak module cannot use the bus continuously.
Central arbiter
→ Round robin priority scheduling
Distributed arbiter
→ The next request cannot be issued until all requesting modules satisfy their requests.
Notes: If the priority level of the arbiter is fixed, the starvation problem may happen. That is, a weak module cannot use the bus continuously. For the central arbiter, the round robin priority scheduling can be implemented. That is the priority level is shifted between modules. For the distributed arbiter, it is hard to be implemented. In this case pheudo round robin method is used.

## Slide 19: Round Robin
Priority
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111
Notes: This diagram shows the round robin priority scheduling. After an arbitration is finished, the priority shifts so that the fairness of the bus is kept.

## Slide 20: Practical Starvation Avoidance
Priority
000
001
010
011
100
101
110
111
Assume that 0 is the strongest.
Blocked
Blocked
Blocked
Blocked
All Blocked modules are released
Notes: Since the round robin scheduling takes cost, a simpler policy is often used. The rule is simple, a module who won the arbitration cannot issue the next request until there is no requesting module. This diagram shows an example.

## Slide 21: Overlap between the arbitration and data transfer
Arbitration
Data transfer
n
n-1
bus master for
n-th transaction
n
n+1
n+1
bus master for
n+1-th transaction
n+2
n+1
bus master for
n+2-th transaction
n+3
So, the arbitration time is not critical in most cases.
Notes: The bus arbitration is usually done overlapped with bus transaction itself. Thus, during a transaction, the next bus master is selected, and the time of bus arbitration is hidden. This is why the speed of arbiter is sometimes not treated as a critical matter.

## Slide 22: glossary-1
Arbiter 調停回路
Arbitration 調停操作、バスマスタを選ぶ
Bus master バスマスタ、バスの利用権を管理するモジュール
Bus slave バススレーブ、バスの利用権を持たないモジュール（マスタからスレーブに常にデータを転送するわけではないので注意！）
Centralized 集中型 ⇔ Distributed 分散型
Daisy Chain Arbiterの一方法で、ヒナゲシの花輪から来ている
Transaction バス上でデータを転送するための一連の操作
Open drain オープンドレイン、バスの作り方の一つで、出力トランジスタをオープンにして抵抗につなぐ。全てがOFFのときのみHレベルになり、どれか一つでもONになるとLレベルになる。この操作をワイヤードORと呼ぶ。
Starvation 飢餓状態、バスの利用権を獲得できない状態が長期間続くこと
Round-robin ラウンドロビン、優先順位をArbitration毎に隣りのモジュールに移動していく方法

## Slide 23: Handshake for data transfer
2-edge
2-line (Strobe + 1 Acknowledge)
4-edge
Only for a single slave
2-edge
3-line (Strobe + 2-Acknowledge)
4-edge
For multiple slaves
Notes: Now, let me explain about the handshake mechanism. For a bus with a single slave, 2-line handshake is enough. If it transfers data with four edges, it is called 4-edge handshake, and with 2 edges, it is called 2-edge handshake. For multiple slaves we need three lines.

## Slide 24: ２-line ４-edge handshake
Strobe
Address/
Data
Acknowledge
Notes: This shows a waveform of the 2-line 4-edge handshake. Here is an example of transferring the data from the master to a slave. The master set the address or data on the bus and assert the strobe. The slave checks the strobe and receives the content on the bus at the negative edge of the strobe signal. After receiving the slave changes the acknowledge low to high. The master removes the content and changes strobe to high. After checking it, the slave returns the acknowledge signal and goes to the next step. This method uses four edges to send one item on the bus.

## Slide 25: ２-line ２-edge handshake
Strobe
Address/
Data
Acknowledge
Data ttem is transferred with both edges of the strobe
Notes: 4 edge handshake is time consuming. So, we can send the next data at the rising edge of the strobe. This is called 2 edge handshake. Address or data are transferred at the both edge.

## Slide 26: In the case of multiple slaves
Strobe
Address/
Data
Module １
Acknowledge
Module ２
Acknowledge
L because 2 is L
Acknowledge
Bus (Wired-OR)
Notes: Two line handshake does not work well when the number of slaves become two or more. In this case, when both slaves receive the data, they turn acknowledge line high. Since open drain bus is used for acknowledge line, it turns high when the slower module changes the level. This diagram seems well.

## Slide 27: Quiz
3-line handshake (1 for strove and 2 for acknowledge) is used for multiple slaves.
Why 2-line handshake cannot manage multiple slaves?
Notes: Let’s think well. Why 2-line handshake cannot manage multiple slaves and another line is needed?

## Slide 28: ２-line cannot manage multiple slaves
Strobe
Address/
Data
Module １
Acknowledge
Module 2 (SLOW!)
Acknowledge
２ is still L
Then, go to next transfer！
OK！
Slow module
Cannot receive
Acknowledge
Bus (Wired-OR＝AND)
Negative edge cannot be used for synchronization
Notes: This diagram illustrates the reason. Assume that the module 2 is extremely slow. Even the case, the acknowledge for receiving data will transferred well because of the wired or bus. When the slower module turns the level high, the bus level becomes high. However, when master wants to go to next step and turns the strobe high. In this case, the acknowledge signal becomes low when the faster module turns the level low. So, the master cannot recognize whether the slower module is ready or not. In this case, the master can go the next bus transaction and misunderstand the acknowledge of the slower module.

## Slide 29: ３-line handshake
Strobe
Address/
Data
Acknowledge １
Acknowledge ２
3-line 2-edge handshake is also possible
OK!
Next transfer
OK!
Positive edges of two acknowledge lines are used in turn
Notes: This problem can be solved by providing another acknowledge signals and using them in turn. In this case, only the rising edge can be used for the handshake, and it certainly becomes high when the slower module turns to high. This diagram shows 3-line 4-edge handshake, but 3-line 2-edge handshake is possible.

## Slide 30: Handshake in the chip
Strobe
Master
slave 1
slave 2
slave n
…
slave 1
slave 2
slave n
…
AND
AND
Master
Ack1
Ack2
Of course, wired-or wire is not used.
The concept itself is not changed.
Notes: Inside the chip, of course, the wired-or wire is not used, but the concept itself is not changed. Two acknowledge signals are used to inform master whether slaves are ready or not.

## Slide 31: Synchronous bus is suitable for block transfer
Strobe
Address/
Data
Acknowledge
Clock
The start/end handshake is the same, but block transfer is possible synchronized with a clock
Notes: Usually, the handshake is required when bus transaction is started. But, the data transfer can be done synchronized with the bus clock, and continuous data transfer can be done. This is why the synchronous bus is suitable for block or burst data transfer. After that, the handshake is taken.

## Slide 32: Non-Split Transaction
Address
Memory reading
Data transfer
Module A
Module B
Bus utilization is degraded
Notes: On the basic bus, the bus is locked during the waiting time. Assume that the module A is a core and module B is a memory. When a core sends an address with reading request, the memory starts reading the data. After the memory is ready, the data block is transferred.

## Slide 33: Split Transaction
データ転送
B→A
Address
Module A
Module B
Module D
Address
Module C
Split transaction of A→B
Transaction C→D is executed
C→D
Notes: For efficient use of such a waiting time, the split transaction is used. After sending the address and reading request, the module A releases the bus. So, the module C can use the bus for its purpose. After the waiting time, the split transaction from B to A starts again. After that, the data transfer from C to D is executed.

## Slide 34: Advanced I/O Buses
PCI bus was widely used, but it could not cope with recent computer system.
  32bit/33MHz, 64bit/66MHz
New standard I/O bus
  PCI-X
    64bit/133MHz DDR/QDR
  PCI Express
    Point-to-point serial data transfer
    1 lane:2.5Gbps
    x2, x4, x8
  Now, PCI Express is used instead of PCI bus.
Notes: As the bus for Personal Computers, PCI bus was widely used until about 1990’s. It was 32bit bus with 33MHz clock and then extended to 64bit with 66 MHz. But, it could not cope with the performance improvement of personal computers. Then, the PCI-X, a straight extension was shortly, but they were replaced with a new concept PCI express. It has been widely used.

## Slide 35: PCI Express
Consisting of serial one-to-one bidirectional connection wires called lanes.
Each lane supports 2.5Gbps/5Gbps (Physical Speed)
Multiple lanes can be used as a link(x4, x8, x16 and x32).
The data is transferred in a packet called TLP (Transaction Layer Packet).
Interconnection network rather than the bus, but the protocol of traditional PCI bus is supported.
port
Physical
layer
port
Physical
layer
lane
link
Notes: PCI Express is actually not a bus in traditional sense, but a serial high speed one-to-one bidirectional connection. There are several bi-directional lanes and form a link. The data is transferred in a packet called TLP or Transaction Layer Packet. It is a packet switching network, but the protocol of old PCI bus is supported.

## Slide 36: PCIe standard
 | Gen1 | Gen2 | Gen3
Physical speed（Gbps） | 2.5 | 5 | 8
Bandwidth (GB/sec) | 0.25 | 0.5 | 1.0
x8 bandwidth (GB/sec) | 2.0 | 4.0 | 7.9
Encoding | 8b/10b | 8b/10b | 128b/130b
Physical speed is x1.6, but almost twice practical performance is realized by
changing the encoding method.
Notes: OK. Let’s review PCIe standard. The physical link speed of Gen3 is 8Gbps, the 1.6 times as that of Gen2. But, by using 128b/130b coding instead of 8b/10b used in Gen2, it achieves almost twice bandwidth that of Gen3.

## Slide 37: An example of bus system using PCI express
CPU
Root Complex
Memory
System bus
Memory bus
Graphics
Switch
Switch
End
point
End
point
End
point
PCI Bridge
PCI bus
PCI
Express
Notes: PCI express is used with a tree like structure. It is connected with CPU through the root complex. It is actually a switch which has multiple links to other switches. I/O modules are connected to end-point.

## Slide 38: On-chip bus
For on-chip implementation, various types of IP (Intellectual Property) must be connected.
Standard bus is required.
  AMBA (Advanced Microcontroller Bus Architecture): a bus for ARM cores.
  CoreConnect: a bus for PowerPC cores.
  Wrapper based buses
    IPs are wrapped in the standard interface.
For further performance improvement, NoCs (Network on Chips) are introduced.
→ Introduced in the later part of this lecture
Notes: There are various types of on-chip bus, but recently network-on-chips or NoCs are becoming used popularly.

## Slide 39: NEC MP211
ARM926
PE0
ARM926
PE1
ARM926
PE2
SPX-K602
DSP
DMAC
USB
OTG
3D
Acc.
Rot-
ater.
Image
Acc.
Cam
DTV
I/F.
LCD
I/F
Async
Bridge0
Async
Bridge1
APB
Bridge0
IIC
UART
TIM1
TIM2
TIM3
WDT
Mem. card
PCM
APB
Bridge1
Bus Interface
Scheduler
SDRAM
Controller
SRAM
Interface
On-chip
SRAM
(640KB)
PLL
OSC
Inst.
RAM
PMU
INTC
TIM0
GPIO
SIO
Sec.
Acc.
SMU
uWIRE
Camera
LCD
FLASH
DDR SDRAM
Ｍｕｌｔｉ－Ｌａｙｅｒ ＡＨＢ
An example of on-chip bus

## Slide 40: Summary of Bus
Classic bus with passive wires has been changed to active bus with a kind of switches
High Speed Bus
  Synchronous bus with Split Transaction
  Using active devices
  It becomes somehow like a packet transfer with switching hub.
Notes: OK. This is a summary of buses.

## Slide 41: glossary 2
Handshake 握手のことだがここでは正しく転送するための信号のやりとりを指す
Synchronous 同期式⇔Asynchronous 非同期式
Strobe 転送を起動を知らせる信号線
Acknowledge Strobeに対する応答用の信号線
Edge 信号線の変化
Split transaction バス転送を中断して途中に他の転送を挟むことを可能にする方法

## Slide 42: Crossbar switch
ｎ
ｍ
Cross point: small
switching element
The number of
cross points:
ｎｘｍ
Extension of the buses
Notes: Today’s next target is a crossbar switch. Some of you may feel strange, because the crossbar is a typical switch. However, the crossbar switch is actually an extension of multiple buses. Here we assume n cores and m memory. Providing small switching elements at the cross points of their individual buses, the crossbar can be built. That is, it requires nxm cross point switches.

## Slide 43: Non-blocking property
ｎ
ｍ
For different
destination,
conflict free
Notes: By make the best use of cross point switches dedicated lines can be formed for the different destination. That is it is conflict free or non-blocking.

## Slide 44: Head Of Line (HOL) conflict
ｎ
ｍ
X
Arbiter is required for each bus
The buffer is required
The number of cross
point is not dominant.
Notes: However, of course, if the destination module is the same the multiple requests conflict with each other. In this case, like common buses, the arbiters are used. Some people call this conflict, head of line or HOL conflict.

## Slide 45: Input buffer switch
Crossbar
Input buffer
One of conflicting packets is selected.
Others are stored Into the input buffer
Notes: When conflict occurs, one of the requests is usually stored in the input buffer or FIFO attached to the crossbar. After another request passing the crossbar, the waiting request is transferred. The similar mechanism can be provided for the bus. Parallel machines commonly use this style so called input buffer switch.

## Slide 46: Output buffer switch
Crossbar
Crossbar must work with ×n frequency of input/output rate.
No HOL problem.
Used in switches in WAN, but for parallel machines it is difficult.
Output buffer
works with ×n freq.
Notes: Some people claim that there is output buffer switch. But, for parallel machine, it is rarely used, because for solving the HOL conflict, the multiple data must be transferred to the output buffer. It means that the output buffer must work with n times clock frequency. This situation is almost impossible for multicore machines.

## Slide 47: Buffers at cross-point
ｎ
ｍ
The buffer is provided
at each cross-point.
High performance but
the total amount of
buffer becomes large.
Notes: Another idea is providing buffers at cross point. It achieves high performance but the total amount of buffer becomes huge.

## Slide 48: An example of a modern router
WH router with two virtual channels
5x5 XBAR
ARBITER
FIFO
FIFO
FIFO
FIFO
FIFO
X+
X-
Y+
Y-
CORE
X+
X-
Y+
Y-
CORE
(Introduced later in this lecture)
Notes: This is a practical design example of a modern router using the crossbar. I will explain this structure later in this lesson.

## Slide 49: Merit/demerit of Crossbars
Non-blocking property
Simple structure/Control
The hardware for cross-points usually do not limit the system (Fallacy of crossbars)
Extension is difficult by the pin-limitation of LSIs
  If pins can be used, a large crossbar can be constructed → Earth simulator
Notes: Here, the pros and cons of crossbars are summarized.

## Slide 50: SUN T1
Core
Core
Core
Core
Core
Core
Core
Core
Crossbar
Switch
FPU
L2
Cache
bank
Directory
L2
Cache
bank
Directory
L2
Cache
bank
Directory
L2
Cache
bank
Directory
Single issue six-stage pipeline
RISC with 16KB Instruction cache/
8KB Data cache for L1
Total 3MB, 64byte Interleaved
Memory
Notes: This is an example of Sun microsystem’s earlier multi core processor.

## Slide 51: The earth simulator
Vector Processor
Vector Processor
…
Vector Processor
0
1
7
Shared Memory
16GB
Vector Processor
Vector Processor
…
Vector Processor
0
1
7
Shared Memory
16GB
Vector Processor
Vector Processor
…
Vector Processor
0
1
7
Shared Memory
16GB
….
Interconnection Network (16GB/s x 2)
Node 0
Node 1
Node 639
Peak performance
40TFLOPS
Notes: Japanese supercomputer “the earth simulator” used a huge crossbar. It connected 639 modules.

## Slide 52: glossary 3
Crossbar switch: クロスバスイッチ、ここでは主としてスイッチ本体を指すが、バッファも入れて考える場合もある
Router:パケットを転送するためのハードウェア全体を指す
WH, Virtual Channel:この授業のもっとあとで紹介するのでここでは深く追求しないでよい
Non-blocking, blocking:出力ポートが重ならなければ、衝突が起きないのがノンブロッキング、出力ポートが重ならなくてもスイッチ内部で衝突するのがブロッキング
HOL conflict:出線競合、出力ポートが重なることで起きる衝突

## Slide 53: Homework 2
Your computer uses PCIe gen2 x 8.
  1. How much maximum bandwidth can be used ?
  2. You want to improve the bandwidth.
  2-1. When you use PCIe gen2 x 16, how much maximum bandwidth can be used?
  2-2. You changed the bus to PCIe gen3 x 8, how much maximum bandwidth can be used?
  Just a simple calculation. You will spend only about 3 minutes.
Notes: OK. This homework is too simple. Maybe you will spend 3 minutes.