## Slide 1: Reconfigurable Architectures
AMANO, Hideharu
hunga＠am．ics．keio．ac．jp

## Slide 2: Reconfigurable System （Custom Computing Machine）
A target algorithm is executed directly with a hardware on SRAM-style FPGA/PLDs.
  High performance of special purpose machines.
  High degree of flexibility of general purpose machines.
A completely different execution mechanism from stored program computers.
Notes: Unlike common computers, in reconfigurable systems or custom computing machines, a target algorithm is executed directly with a hardware on SRAM-style FPGA/PLDs. It can provide both high performance of special purpose machines and high degree of flexibility of general purpose machine. That is to learn about reconfigurable systems is to learn hardware algorithms.

## Slide 3: What is PLD(Programmable Logic Device)?
Integrated Circuit whose logic function can be defined by users.
  ↔ Standard ＩＣ，ＡＳＩＣ(Ａｐｐｌｉｃａｔｉｏｎ Ｓｐｅｃｉｆｉｃ ＩＣ）
ＳＰＬＤ（Simple PLD) / ＰＬＡ（Programmable Logic Array)
  Small scale IC with AND-OR array
ＣＰＬＤ(Complex PLD)
  Middle scale IC with AND-OR array
ＦＰＧＡ（Ｆｉｅｌｄ Ｐｒｏｇａｒｍｍａｂｌｅ Ｇａｔｅ Ａｒｒａｙ）
  Large scale IC with LUT
Notes: First of all, let’s review programmable logic devices or PLDs quickly. It is an integrated circuit whose logic function can be defined by users. It is an opposite concept as that of standard IC or ASIC which cannot change its hardware. It is classified into small SPLD or PLA, middle scale Complex PLD and FPGAs. Though SPLD and CPLD are still used in some specific area, FPGAs are most popularly used recently.

## Slide 4
1990
2000
1980
10K
100K
1M
10M
Gate number
Increasing Performance
From 1991-2000
Amount of gate: X45
Speed: X12
Cost:1/100
Fuse-
PLA
EEPROM-
SPLD
SRAM-
FPGA
CPLD
Anti-fuse
FPGA
Hierarchical structure
Embedded Core
Low voltage
Rapidly development of PLD
Notes: The first PLDs used in 1970’s were fuse type programmable logic array. Since the program is done by breaking fuses, it is programmable only once. In mid 80’s, EEPROM style SPLD called GALs which is rewritable were popularly used. FPGAs appeared in the early 90’s. It grew up rapidly until now.

## Slide 5: LUT：Look Up Table
Look Up Table
ROM/RAM
…
Address
…
Data
A simple ROM/RAM can used as a
random logic.
ABC
０００
００１
０１０
０１１
１００
１０１
１１０
１１１
Z
０
０
０
１
０
０
０
１
Z
０
０
０
１
０
０
０
１
C
B
A
A combination of memory and
multiplexers are commonly used.
Notes: A simple ROM or RAM can be used as a logic circuit by storing truth table and reading it by address as inputs of the circuits. However, since the common memory focuses on the storing data as much as possible, it is not efficient when used for truth table. Instead, a small register and a tree of multiplexer is advantageous considering both speed and cost. This structure is called a look up table or LUT.

## Slide 6: An example using LUT：Look Up Table
ABC
０００
００１
０１０
０１１
１００
１０１
１１０
１１１
Z
０
０
０
１
０
０
０
１
Z
０
０
０
１
０
０
０
１
C
B
A
1 1 0
1
Notes: Each multiplexer shares the control signal in each hierarchy, and the lower input is selected when 1 is given, while the upper input is selected when 0 is given. You can easily see that the table is referred with this mechanism.

## Slide 7: FPGA(Field Programmable Gate Array)
LUT
F.F
Configurable Logic
Block
Switch
Block
Connection Block
IOB
island style
LUT and interconnection
is decided with
configuration data
Notes: This diagram shows the island style FPGA. Two LUTs and Flip flops form a unit of logic called configurable logic block or CLB. They are distributed in the sea of wires. At the intersection of wires and the input/output of CLB, there are switch blocks consisted of simple MOS FET. If they are ON, the wires are connected, otherwise, they are separated. The content of LUTs and the ON/OFF control of theses switches is stored in the SRAM distributed to all around of the chip. The circuits configuration is decided by the data, so it is called configuration data.

## Slide 8: Various PLDs
SPLD
CPLD
FPGA
Anti-fuse
EEPROM
Flash-ROM
SRAM
High speed middle size
One-time
ACTEL，Quicklogic
Large scale
Rapidly development
Xilinx、Altera
High speed small/middle size
Re-programmable
Delay is predictable
Lattice，Altera，Xlinx
Notes: There are several architecture styles and technologies to make the circuits flexible. Anti-fuse techniques, EE PROM or Flash-ROMs have been utilized. However, the FPGA which uses SRAM has been rapidly developed and widely used.

## Slide 9: Why SRAM style FPGAs ?
Cons:
  Configuration data disappears when power is shut-off.
  Small ROM or a host which makes the configuration is required.
Pros:
  In-system programming is possible.
    The design can be changed dynamically.
  The common CMOS process can be used.
Notes: Why SRAM style FPGAs has become so popular. There is a big problem of this type. Configuration data disappears when power is shut-off. So, configuration data must be reloaded at the power on from an on-board small ROM or a host computer. The benefit is its flexibility, that is the design can be changed dynamically. It is a good property for a reconfigurable system introduced later. But, the largest advantage is that the common CMOS process can be used in SRAM style FPGAs. That is, it can use the most advanced CMOS technology without special technology for EE-ROM or anti-fuse.

## Slide 10: Recent trends on FPGAs
2015 Intel acquired Altera.
  Big-two era: Intel vs. Xilinx
Large and sophisticated configurable blocks
IPs/SoC style FPGA
2.5D implementation
Partial Reconfiguration
Notes: In 2015, Intel acquired Altera, and until now, FPGA business is lead by two major companies. Intel versus Xilinx. Now, the configurable block of an FPGA becomes complicated, and various types of Intellectual Properties have been introduced. 2.5D implementation and the partial reconfiguration are also new technologies.

## Slide 11: Xilinx Virtex II
Programmable IOs
Configurable Logic
DCM
IOB
RAM
Multiplier
Global
Clock
MUX
LUT
Carry
D
Q
LUT
Carry
D
Q
Slice
Slice X 2 → CLB (Configurable Logic Block)
100000 CLBs
3Mbit
Notes: This shows the diagram of the second generation FPGA. Unlike a simple island style FPGA, a carry logic which connects neighboring CLBs was introduced. Between CLBs, standard intellectual properties such as embedded RAM and multiplexers have be implemented. Clock control modules and buffers were also provided.

## Slide 12: Slice structure of Virtex-6
LUT
6inX1
5inX2
Carry
FF
FF
MUX
6bit
MUX
LUT
6inX1
5inX2
Carry
FF
FF
MUX
6bit
MUX
LUT
6inX1
5inX2
Carry
FF
FF
MUX
6bit
MUX
LUT
6inX1
5inX2
Carry
FF
FF
MUX
6bit
MUX
Virtex-6 manual
Notes: This diagram shows the configuration element called slice in the recent FPGAs. The number of LUT is increased to 6, and the output circuits became complicated and flexible.

## Slide 13: Virtex-6 CLBs
Slice
X0Y0
Slice
X1Y0
CLB
COUT
COUT
Slice
X2Y0
Slice
X3Y0
CLB
COUT
COUT
Slice
X2Y1
Slice
X3Y1
CLB
COUT
COUT
Slice
X1Y0
Slice
X1Y1
CLB
COUT
COUT
CIN
CIN
CIN
CIN
Virtex-6 manual
Notes: Slice means a half of configurable logic in Xilinx’s FPGAs. The carry logic connects the slice of the neighboring slice, not another slice in the same CLB.

## Slide 14: Intel (Altera) Stratix II
Mega RAM
Blocks
M4K RAM
Blocks
M512 RAM
Blocks
PLL
DSP Blocks
LAB：Logic Array Block
consisted of 10 LE (
4-input LUT and F.F.)
Hierarchical Interconnect
Notes: Intel uses Logic Array Block consisted of 10 logic elements. Between LABs, a large RAM blocks and DSP blocks are provided. DSP means digital signal processing but actually it is a multiply-and-add units.

## Slide 15: Stratix-IV ALM Structure
LUT
6in
FF
MUX
4bit
data
MUX
LUT
6in
adder1
FF
MUX
4bit
data
MUX
adder2
shared_arith
carry
reg_carry
4-in LUT X 2
5-in LUT + 3-in LUT
5-in LUT + 4-in LUT 1-input shared
5-in LUT + 5-in LUT 2-input shared
6-in LUT
6-in LUT + 6-in LUT 4-input shared
Stratix-IV manual
Notes: The Logic element of Stratix-IV uses two 6-input LUTs sharing with several inputs. These combination can be selected. So, it is called Adaptive Logic Module. The carry and sophisticated output logics are somehow like that of Virtexs’.

## Slide 16
LAB
Local
Interconnect
MLAB
Local
Interconnect
ALMs
Stratix-IV LAB structure
Stratix-IVマニュアルより
Notes: Stratix IV’s logic modules are connected with local interconnect then connected with global connection module. Hierarchical interconnect reduces the latency between logic blocks. So, high frequency clock can be used.

## Slide 17
Technologies vs. Product
90nm
65nm
45nm 40nm
Virtex-4LX/FX/SX
200000LC
Stratix-IV
/E/GX/GT
531200LE
Stratix-III/L/E
338000LE
Stratix-II/GX
179400LE
Cyclone IV/E/GX
149760LE
60nm
Cyclone III/LS
119088LE
Cyclone II
68416LE
Virtex-6LXT/SXT/
HXT/CXT
760000LC
Spartan-6LX/LXT
150000LC
Virtex-5LX/LXT/SXT/
FXT/TXT
330000LC
Spartan-3A N/DSP
53000LC
High-end
Low-cost
28nm
Virtex-7
T/XT/HT
2000000LC
Stratix-V
/E/GX/GS/GT
359200ALM
Cyclone V
/E/GX/GS/GT
301000LE
Arria
Arria-II
Arria-IV
174000LE
Kintex-7
480000LC
Artix-7
360000LC
Middle range
X1.5-X2.5／generation
High-end/Low-cost: X3－X5
Notes: Xilinx and Intel have used advanced semiconductor processes. That is, as soon as the new technologies were available, they developed a new series. They have two series: high-end and low-cost, and later, mid-range products were added.

## Slide 18
Technology vs. Products (Cont.)
28nm
Virtex-7
2000000LC
Stratix-V
/E/GX/GS/GT
359200ALM
Cyclone V
/E/GX/GS/GT
301000LE
Arria-IV
174000LE
Kintex-7
480000LC
Artix-7
360000LC
20nm
16nm
Virtex-Ultrascale
5541000LC
Virtex-Ultrascale＋
3780000LC
Kintex-Ultrascale
1451000LC
Kintex-Ultrascale＋
1143000LC
Arria-10
ARM＋FPU
Stratix-10
ARM＋FPU
10nm
Notes: Now, the most advanced high end products use 10nm process technology. Xilinx is trying to introduce AI accelerator in a new FPGA series. Intel developed products also focuses on AI acceleration.

## Slide 19: IP（Intellectual Property) and SoC FPGA
Standard IP
  Embedded RAM
  Multiplier, DSP module（Multiplier＋ALU)
  Clock Manager
  High Speed serial I/O
Special IPs
  PCI Express Interface
  Ethernet MAC controller
  DRAM Memory Controller
  CPU → SoC Style FPGA
  Arria 10、Stratix 10
Notes: The key of recent FPGAs is IP (Intellectual Property). They have various types of standard IP, and some FPGAs have specialized IP. Recently, hard core CPU has been integrated. These products are called SoC.

## Slide 20: Zynq All programmable SoC
ARM Cortex-A9（PS part) Dual Core CPU +
28nm Artix-7/Kintex-7 based FPGA（PL part)
Notes: Xilinx Zynq all programmable SoC has ARM Cortex A9 dual core CPU with programmable logic corresponding to Artix-7/Kintex-7. Recent Zynq-ultrascale+ has powerful ARM CPUs and programmable logic of high end FPGAs. Although it is rather for embedded systems, Linux runs on the ARM CPU, and the communication between CPU and FPGA can be done through the standard AXI bus.

## Slide 21
Zynq-7000 All Programmable SoC
MIO
Processing System (PS)
Programmable Logic (PL)
APU
DRAM Controller
2 SPI
2 SD SDIO
2 GigE
2 USB
GPIO
2 I2C
2 CAN
2 UART
Flash Controller
(NOR, NAND,
SRAM, QSPI)
ARM Cortex-A9
32/32 KB
I/D Cache
512Kbyte L2 Cache
Snoop Control Unit
256Kbyte On-Chip Memory
AXI Interconnect
ARM Cortex-A9
32/32 KB
I/D Cache
AXI Interconnect
General Purpose
AXI ports
AXI ACP
High Performance
AXI ports
Notes: Various types of I/O controllers are provided on the CPU part of Zynq. It can be also accessed from FPGA part.

## Slide 22: Zynq-Ultrascale+
Zynq-Ultrascale+
Zynq: xczu19eg-ffvc1760
GTH link x8
GTY link x4
DRAM 16Gb PL
4Gb PS
Gb Ethernet
USB 3.0

## Slide 23: 2.5D FPGA (http://www.xilix.com)
Notes: Recent large scale FPGAs are implemented with multiple chips. on the silicon interposer. For example Zynq-ultrascale+ consists of two chips: one is ARM CPU and the other is FPGA. Even mid-renge Kintex Ultrascale uses 2.5D structure. Although the cost can be reduced, the wires between two chips often form the bottleneck.

## Slide 24: FPGA as an accelerator
Stratix 10
  14nm Intel process
  HyperFlex which enables GHz clock.
    Registers are provided on the wires.
  FP DSP modules with 10TFLOPS max.
  ARM Cortex A53 Quad Core
Arria 10
  20nm TSMC process
  1.5TFLOPS max.
Open CL is used for programming
Notes: Intel’s high end FPGAs have been designed to use an accelerator like GPUs. It provides a powerful floating point DSP modules up to 10TFLOPS at maximum. HyperFlex architecture which inserts registers on the wiring resource enables to use more than 1GHz system clock. They are supposed to be used for learning and recognition phase of Deep Learning.

## Slide 25: Partial Reconfiguration
A part of configuration on FPGA can be replaced during operation.
  .Since Virtex-4, most of Xilinx’s FPGAs provide it.
  Intel’s FPGAs also provide it since Stratix V.
The FPGA is divided into the shell part which provides I/O, and user logic part which is partially reconfigured.
Easy to be implemented in recent FPGAs.
Notes: Partial reconfiguration has been provided inmost recent FPGAs. It can make configuration of a part of FPGA, while other parts are working. By using this function, the FPGA is divided in the shell part provides I/O and user logic part which is partially reconfigured. It has become indispensable function for an FPGA as an accerelator.

## Slide 26: Partial Reconfiguration
Reconf
Frame
Clock Region Boundary
PRM
PRM(Partial Reconfigurable Module) is placed on a fixed frame.
The problem is the interconnection between partial reconfiguration module
and static part.
Notes: The area of partial reconfiguration has limitation.

## Slide 27: Partial Reconfiguration area for Xilinx Kintex Ultrascale
Notes: This shows an example for Kintex Ultrascale

## Slide 28
Partial Reconfiguration region
The case of Altera(Intel)’s Stratix V
Notes: This is the case of Intel’s Stratix V.

## Slide 29
Replacing with another accelerator
Main switching fabrics works without stopping.

## Slide 30: Reconfigurable System （Custom Computing Machine）
A target algorithm is executed directly with a hardware on SRAM-style FPGA/PLDs.
  High performance of special purpose machines.
  High degree of flexibility of general purpose machines.
A completely different execution mechanism from a stored program computers.
Notes: Reconfigurable Systems or custom computing machines are systems in which a target algorithm is executed directly with a hardware on SRAM-style FPGA/PLDs. It aims to get high performance of special purpose machines with high degree of flexibility of general purpose machines. A completely different execution mechanism from a stored program computers is used.

## Slide 31
Flexibility
Performance
CPU
for i=0; i<K; i++
X[i]=X[i+j]
.....
CPU
Software
ASIC
Design
A
Design
C
Design
D
Design
B
FPGAs
High Performance and Flexibility
Refonfigurable Systems
Notes: This diagram explains the stand point of reconfigurable systems.

## Slide 32: How to enhance the performance？
Performance enhancement by hardware execution itself
  The overhead of software execution (Instruction fetch, data load to registers, and etc.)
  The overhead of using fixed size data.
  The overhead of using only two way branches.
The key of performance improvement is parallel processing
However, these benefits are not so large, for embedded CPU and DSP
are highly optimized.
Notes: People might think that the performance of program can be improved just by implementing hardware. However, performance enhancement by hardware execution itself comes from these issues. However, their effect is not so large, since the embedded CPU and DSP are highly optimized. The key of performance improvement is parallel processing.

## Slide 33: Parallel processing in reconfigurable systems
Various techniques can be used
  SIMD execution
  Pipelined structure
  Systolic algorithm
  Data driven control
Parallel execution other than calculation
  Parallel data access using internal memory units
  Parallel data transfer including I/O accesses
Notes: In reconfigurable systems, various techniques which have been introduced in this lesson can be used.

## Slide 34: SIMD (Single Instruction-stream/ Multiple Data-stream)-like calculation
Stream Data in
Stream Data out
Internal
Memory module
Processing part
The same instruction is applied to different data stream
In Reconfigurable Systems, the operation is not required to be same
（SIMD-like calculation）
Notes: On reconfigurable systems, SIMD can be used widely. The processing can be changed since the operation can be embedded in the processing element.

## Slide 35: Pipelined structure
Stream Data １
Stream Data １
Internal
Memory module
Processing part
The stream is divided and inserted periodically.
Stream Data 2
Stream Data 3
Stream Data 4
Stream Data 5
Stream Data 2
Notes: Pipeline execution or stream execution can be also used. Since the I/O is often limited, this type of execution is widely used in reconfigurable systems.

## Slide 36: Systolic Algorithm
Data x
Data y
Computational array
Data stream x，y are inserted with a certain interval.
When two streams meet each other, a calculation is executed.
→ Systolic: The beat of heart
Notes: Systolic Algorithm is classic hardware algorithm frequently used on reconfigurable systems. It consists of homogeneous simple processors or cells which send and receive data from/to other cells periodically. The data stream x, and y are inserted with a certain interval. When two streams meet each other, a calculation is executed. Systolic means the beat of heart. It is also used in Googles’ domain specific system Tensor Processing Unit.

## Slide 37: Band matrix multiply y=Ax
a
x
a11 a12 0 0
a21 a22 a23 0
0 a32 a33 a34
0 0 a43 a44
Ｘ＋
ｙｉ
ｙｏ
ｙｏ＝ ａ ｘ ＋ ｙ ｉ
y0
y1
y2
y3
x0
x1
x2
x3
=
Notes: It is a cell which calculates the band matrix. Each cell receives x from left, y from right, and a from up. Then computer a x + y, and sends the result to left direction.

## Slide 38: Band matrix multiply y=Ax
Ｘ ＋
a11
x1
a12 a21
a22
a23 a32
a11 a12 0 0
a21 a22 a23 0
0 a32 a33 a34
0 0 a43 a44
Notes: First x1 means a11 at the central cell.

## Slide 39: Band matrix multiply y=Ax
Ｘ ＋
Ｘ ＋
x1
a12 a21
a22
a23 a32
a11 a12 0 0
a21 a22 a23 0
0 a32 a33 a34
0 0 a43 a44
a33
y1=a11x1
x2
Notes: The computation is done at the both side cells.

## Slide 40: Band matrix multiply y=Ax
X ＋
x1
a34 a43
a22
a23 a32
a11 a12 0 0
a21 a22 a23 0
0 a32 a33 a34
0 0 a43 a44
a33
y2=a21 x1
x2
x3
y1=a11 x1+
a12 x2
Notes: This time the central cell computes again.

## Slide 41: Band matrix multiply y=Ax
Ｘ ＋
Ｘ ＋
a34 a43
a44
a23 a32
a11 a12 0 0
a21 a22 a23 0
0 a32 a33 a34
0 0 a43 a44
a33
y2=a21 x1+
a22 x2
x2
x3
Notes: The side cells executes again.

## Slide 42: Band matrix multiply y=Ax
Ｘ ＋
a34 a43
a44
a11 a12 0 0
a21 a22 a23 0
0 a32 a33 a34
0 0 a43 a44
a33
y2=a21 x1+
a22 x2+
a23 x3
x2
x3
y3= a32 x2
Notes: The central cell computes in turn.

## Slide 43: Data flow algorithm
ｘ
＋
ｘ
＋
ａ
ｂ
ｃ
ｄ
ｅ
（ａ＋ｂ）ｘ（ｃ＋（ｄｘｅ））
The process is activated
with the available of tokens
(data)
The overhead of synchronization is large.
Notes: Data flow algorithm can be also used in reconfigurable system. The computation starts when both input data or tokens are ready.

## Slide 44: Data flow analysis and hardware generation
Data Flow Language
Configuration
Data
Data Flow Graph
Graph Decomposition
HDL
Description
Suitable for automatic generation of hardware
Notes: If the target data flow graph is extracted from some language, it is easy to be changed into HDL description and executed on reconfigurable systems.

## Slide 45: Applications
No flexible program change
No IEEE standard floating point → FPGA as an accelerator
Not memory bounded
  Image processing, analysis, pattern matching,
  Logic simulation, Fault simulation.
  Neural network simulation.
  Encryption /Decryption
  Queuing Model、Markov Analysis
  Electric Power Flow
  Censer processing
Efficient use of on the fly processing.
  Communication control、Protocol control
  Software radio
Notes: They are representative application. Floating point computation is not suitable to reconfigurable systems, since the performance is difficult to be enhanced compared with that of GPUs. However, recent special FPGAs have competitive performance as an accelerators.

## Slide 46: Large Scale Reconfigurable Platforms
…
μP
μP
…
…
RU
RU
…
…
μP
μP
…
RU
RU
Interconnection/Shared memory
…
μP
RU
…
μP
RU
…
μP
RU
…
μP
RU
Interconnection/Shared memory
Hetero nodes using homo cores： SRC6, SGI RASC
Homo node using hetero cores： Cray XD-1, XT4(XR-1)
μP
Stand-alone： SPLASH, RASH,BEE2
…
RU
RU
…
RU
RU
…
RU
RU
Interconnection/Shared memory
Notes: Large scale reconfigurable platforms are classified into three categories. The homo-node using hetero cores are recent trend for FPGA as an accelerator or FPGAs in cloud.

## Slide 47
CRAY-XD1：
AMD Opteron
1board is consisting of 2CPUs＋FPGA（Virtex II Pro)
1 rack provides 6 boards
A high speed network called Rapid Array is used
Interconnection between FPGAs can be done with Rocket I/O

## Slide 48: Microsoft’s Catapult
CPU
FPGA
CPU
FPGA
CPU
FPGA
CPU
FPGA
CPU
FPGA
CPU
FPGA
CPU
FPGA
CPU
FPGA
FE
FFE0
FFE1
Compress
MLS0
MLS1
MLS2
Rank computation for Web search on Bing.
Task Level Macro-Pipelining (MISD)
FE: Feature Extraction
FFE: Free Form Expression: Synthesis of feature values
MLS: Machine Learning Scoring
2-Dimensional Mesh is formed (8x6) for 1 cluster.
FPGA: Altera’s Stratix V

## Slide 49: FPGA-in-Cloud
Host
PC
FPGA
PCIe
Host
PC
PCIe
Host
PC
PCIe
…
FPGA
FPGA
…
  FPGA in the Cloud: Booting Virtualized Hardware Accelerators with OpenStack [FCCM2014]
  Microsoft Catapult [ISCA2014 ][HEART2017]
  FPGA Supervessel Cloud by IBM[ICFPT2016]
  Amazon EC2 F1 Instance [https://aws.amazon.com/ec2/instance-types/f1/]
Not suitable for timing critical jobs.
The total cost becomes large.
  High performance FPGAs are still expensive.
The size of FPGA is limited.
  Multiple FPGAs cannot be used together.
Notes: Recently, there are a lot of activities around FPGA-in-cloud. Most of conventional FPGA-in-cloud uses high performance FPGA boards each of which is attached into its own host. They are connected with network through its host. This natural way has two problems. First, the total cost becomes large, since a number of high performance expensive FPGAs are used. Second, the user can use each FPGA independently but cannot use multiple FPGAs together, since they are separated thorough its host.

## Slide 50: Splash-2 (Arnold et.al 92)
String matching, Image processing, DNA matching, 330 times faster than the supercomputer Cray-II.
Systolic algorithm
VHDL, Parallel C
Annapolis Micro Systems（WILDFIRE)
Notes: The root of stand-alone multi-FPGA system would be Splash/Splash-2. It uses systolic algorithm.

## Slide 51: Flow-in-Cloud (FiC) overview
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
STDM switch
STDM switch
STDM switch
STDM switch
FPGA
STDM switch
STDM switch
STDM switch
STDM switch
Circuit switching network
HLS modules
FiC-SW
Host CPU
I/O board
KCU1500
High Speed Serial Links
Notes: Flow-in-Cloud is consisted of tightly connected FPGA boards each of which provides a cost-efficient FPGA. A host CPU is connected with an I/O board. It is consisting of Xilinx’s XCU1500 and small daughter boards. 9.9G firefly cables are provided to connect other boards. Each board is called FiC-SW, but it provides HLS acceleration module in its partial reconfiguration region.

## Slide 52: FiC(Flow in Cloud)
Stand-alone multi-FPGA
system with 24 boards
Notes: This is a photo of FiC working with 24 boards.

## Slide 53: Historical flow of computer systems
ENIAC
EDVAC、EDSAC
IBM machines
RISC, Intel’s microprocessors
Reconfigurable
Machine
Notes: Reconfigurable machines are another possibility of the computer architecture.

## Slide 54: Exercise
There is a systolic array which multiplies 8 x 8 tri-diagonal matrix A with a size 8 vector x. Compute the number of clock cycles for the multiply. Here, the time when the first element of x reaches to the left-most array is assumed to be time 0.
Notes: Here is today’s exercise.